## Slide 1
Francis Kofi Forson (Professor)
Department of Mechanical Engineering
Kwame Nkrumah University of Science and Technology, Kumasi, Ghana
THERMODYNAMICS I
(ME 265)

## Slide 2: Course Content
Introduction (Definitions and Concepts)
First Law of Thermodynamics
Second Law of Thermodynamics
Properties of Liquids and Vapours
Vapour Power Cycles: Rankine Cycle

## Slide 3: References/Reading List /Recommended Textbooks
Lecture Materials (Notes and Slides)
Y. A. Cengel and M. A. Boles (2019). Thermodynamics: An Engineering Approach 9th Edition.
M.J. Moran, H. N. Shapiro, D. D. Boettner, M. B. Bailey (2018). Fundamentals of Engineering Thermodynamics 9th Edition.
R. K. Rajput (2007). Engineering Thermodynamics 4th Edition.

## Slide 4: ASSESSMENT
Hard copies of two online quizzes would be given to students on day 1 of lectures on 17/01/2022
Quiz 1 will be conducted online between 8am and 12 midnight on 15/02/2022. When you log in into the system to start the quiz, you have 2 hours to complete the questions. Note that you have only one attempt to select the correct answer to each question.
Quiz 2 will be conducted online between 8am and 12 midnight on 5/04/2022. When you log in into the system to start the quiz, you have 2 hours to complete the questions. Note that you have only one attempt to select the correct answer to each question.
Weightings of quizzes and exams | Continuous Assessment (30%) Quiz 1 10% Quiz 2 10% Mid- Semester 10% | Final Examination (70 %) Section A: 49 % Section B: 51 %

## Slide 5: THERMODYNAMICS I (ME 265)
Francis Kofi Forson (Professor)
Department of Mechanical Engineering
Kwame Nkrumah University of Science and Technology, Kumasi, Ghana
INTRODUCTION
(Basic Concepts and Definitions)

## Slide 6: Introduction
Thermodynamics is concerned with the study of energy, its forms and transformations, and the interactions of energy with matter.
Thermodynamics is both a branch of physics and an engineering science.
Engineers are generally interested in studying systems and how they interact with their surroundings. To facilitate this, engineers extend the subject of thermodynamics to the study of systems through which matter flows.
What is thermodynamics?

## Slide 7: Introduction
Systems may be studied from the macroscopic or microscopic approach.
The macroscopic approach to thermodynamics is concerned with the gross or overall behaviour. This is sometimes called classical thermodynamics.
The microscopic approach, is concerned directly with the structure of matter. It is known as statistical thermodynamics.
The macroscopic viewpoint is what is generally adopted in engineering thermodynamics but for understanding concepts are interpreted from the microscopic viewpoint.
Two Approaches to Thermodynamics

## Slide 8: Introduction
Four laws of thermodynamics are:
Zeroth law
First law
Second law
Third law
The state postulate
  Laws of Thermodynamics

## Slide 9: Zeroth Law of Thermodynamics
If Body A has same temperature as body C and body B has same temperature as C, then A and B have the same temperature. This forms the basis for comparison of temperatures.
The Zeroth Law states that, if two systems are in thermal equilibrium with a third system, then the two systems are equally in thermal equilibrium with each other.
The third body or system is usually a thermometer.
A
B
C

## Slide 10: First Law of Thermodynamics
It obeys the conservation of energy which states that energy can neither be created nor destroyed but can be transformed from one form to other.
If a system does not interact with its environment in any way then no energy comes in and no energy goes out. Energy is “conserved”.
There is always an energy balance.

## Slide 11: Second Law of Thermodynamics
Aspects of Second Law include;
Predicting the direction of processes.
Establishing conditions for equilibrium. determining the best theoretical performance of cycles, engines, and other devices.
Evaluating quantitatively the factors that preclude attainment of the best theoretical performance level.

## Slide 12: Third Law of Thermodynamics
It states that, it is impossible to attain a temperature of absolute zero.
On the Kelvin temperature scale, T = 0K is often referred to as absolute zero.
If absolute zero temperature (0K) can be obtained, 100% efficiency can be achieved.

## Slide 13: Applications of Thermodynamics

## Slide 14: Basic Concepts and Definitions
Thermodynamic system is a region of space or an amount of matter, bounded by an arbitrary surface.
Everything external to the system is considered to be part of the system’s surroundings.
The system is distinguished from its surroundings by a specified boundary, which may be at rest or in motion.
A boundary is a closed surface, either real or imaginary, surrounding a system through which energy and mass may enter or leave the system and which separates the system from its surroundings.
Permeable and process boundaries allow mass transfer to occur.
A diathermal boundary allows heat transfer to occur across it as in the case of thin metal walls.

## Slide 15: Basic Concepts and Definitions
Once the system is defined and the relevant interactions with other systems are identified, one or more physical laws or relations are applied.
The system is whatever we want to study. We may want to study a quantity of matter contained within a closed, rigid-tank, or we may want to consider something such as a gas pipeline through which matter flows.
Note:
Even vacuum which is devoid of matter, may be the focus of interest. The composition of matter inside a system may be fixed or may be changing through chemical or nuclear reactions. The shape or volume of the system being analysed is not necessarily constant, as when a piston compresses a gas in a cylinder or a balloon is being inflated.

## Slide 16: Basic Concepts and Definitions
Classification of Systems
A thermodynamic system interacts with its surroundings through its boundary in two ways: by exchanging energy and matter (mass).
Types of systems
Closed system.
Open system
Isolated system

## Slide 17: Basic Concepts and Definitions
Sign Convention
Energy interaction occurs in two ways; heat and work.

## Slide 18: Basic Concepts and Definitions
Thermodynamic Properties
A property is a characteristic of a system. It is used to specify the condition of that system.
The most common properties are pressure, temperature, mass, volume and energy.
A property must be macroscopic, measurable and have a single numerical value that does not depend on how the condition of the system was attained.
Thermodynamic properties are classified as Intensive and Extensive properties.
Extensive properties depend on the extent or size of the system and hence vary directly with the mass. Examples are mass, volume, energy.
Intensive properties are independent of the size of the system. Examples are Pressure, specific volume, specific energy, and temperature.
Specific properties (denoted by lower case letters) are defined as the value of an extensive property per unit mass. They are therefore, independent of mass and are regarded as intensive properties.

## Slide 19: Basic Concepts and Definitions
Three measurable intensive properties that are particularly important in engineering thermodynamics are specific volume, pressure, and temperature.
Specific Volume on mass and molar basis
The density (ρ), or local mass per unit volume, is an intensive property that may vary from point to point within a system. Thus, the mass associated with a particular volume V is determined in principle by integration
and not simply as the product of density and volume.
The specific volume on mass basis v is defined as the reciprocal of density
Like density, specific volume is an intensive property and may vary from point to point. SI units for density and specific volume are kg/m3 and m3/kg, respectively.
The specific volume on molar basis is defined in terms of the specific volume on mass basis by the relation
The specific weight (γ=Weight/V=mg/V) is defined as the weight per unit volume of a system. It is related to the density of the system by the relation: γ = ρg, where g is the local acceleration due to gravity. Specific weight has the unit Newton per cubic meter (N/m3)

## Slide 20: Basic Concepts and Definitions
Pressure
The thermodynamic pressure, P, of a system is defined as the total normal force, per unit area, exerted by the system within and at the boundary. In solids, the pressure is referred to as the normal stress.
The SI unit of pressure and stress is the Pascal (Pa).
1 Pascal = 1 N/m2
It is, however, convenient to work with multiples of the Pascal: the kilopascal, the bar, and the megapascal.
1 kPa = 103 N/m2
1 bar = 105 N/m2 = 100 kPa
1 MPa = 106 N/m2 = 1000 kPa
Another unit of pressure that continues to be used is the atmosphere (atm.).
1 atm = 101 325 Pa =101.325 kPa = 1.013 25 bar = 760 mm Hg
The 760 mm Hg refers to the height of mercury column that the atmosphere can support; the force per unit area exerted by the mercury column is the atmospheric pressure.
The pressure of a system is usually measured relative to its surroundings, and it is called “gauge pressure”. The pressure used in thermodynamics is the absolute pressure and is defined by:
Absolute pressure = gauge pressure + surrounding pressure
Gauge pressure below surrounding pressure is gauge negative and is referred to as vacuum pressure.
p(vacuum) = (absolute) – p(absolute)

## Slide 21: Pressure Measurement in a Column of Static Fluid
Two commonly used devices for measuring pressure are the manometer and the Bourdon tube. Manometers measure pressure differences in terms of the length of a column of liquid such as water, mercury, or oil.
The manometer shown in Fig. 12 has one end open to the atmosphere and the other attached to a closed vessel containing a gas at uniform pressure.
The difference between the gas pressure and that of the atmosphere is given by
A Bourdon tube gauge is shown in Fig. 13. The figure shows a curved tube having an elliptical cross section with one end attached to the pressure to be measured and the other end connected to a pointer by a mechanism.
When the fluid under pressure fills the tube, the elliptical section tends to become circular, and the tube straightens.
This motion is transmitted by the mechanism to the pointer. By calibrating the deflection of the pointer for known pressures, a graduated scale can be determined from which any applied pressure can be read in suitable units.
Because of its construction, the Bourdon tube measures the pressure relative to the pressure of the surroundings existing at the instrument. Accordingly, the dial reads zero when the inside and outside of the tube are at the same pressure.
Figure 12 Figure 13

## Slide 22: Basic Concepts and Definitions
Temperature
If two bodies are kept together for a sufficiently long period, experience shows that the bodies appear to attain the same degree of hotness and the changes in their resistance also cease.
This state is defined as the state of thermal equilibrium, and the two bodies are then said to have the same temperature.
Temperature is, therefore, a property of a system which determines whether or not they are in thermal equilibrium with other systems or their surroundings.
The Celsius, Rankine and Fahrenheit Scales
The Celsius temperature scale uses the unit degree Celsius (°C), which has the same difference in magnitude as the Kelvin.
Thus, temperature differences are identical on both scales. However, the zero point on the Celsius scale is shifted to 273.15 K, as shown by the following relationship between the Celsius temperature and the Kelvin temperature
(1.1)
Thus, from Equation (1.1) we see that on the Celsius scale the triple point of water is 0.01 °C and 0 K corresponds to – 273.15 °C. The ice point is 0 °C.
The temperature of at the steam point, 373.15 K is 100.0 °C. Accordingly, there are 100 Celsius degrees in this interval of 100 Kelvin.

## Slide 23: Basic Concepts and Definitions
The Rankine scale
the unit is the degree Rankine (°R), and is proportional to the Kelvin temperature according to
(1.2)
The Rankine scale is also an absolute temperature scale.
The Fahrenheit scale is related to the Rankine scale by the relation
(1.3)
Substituting Eqs. 1.1 and 1.2 into Eq. 1.3, it follows that
(1.4)
Equation (1.4) shows that the Fahrenheit temperature of the ice point (0 °C) is 32 °F and the steam point (100 °C) is 212 °F.
When dealing with temperature interval on the different scales defined the following must be noted:
During a heating process, the temperature of s system rises by 10 0C. This rise in temperature in K is 10 K. The rise in temperature in 0F is 1.8(10) = 18 0F.

## Slide 24: Basic Concepts and Definitions
INTERPOLATION
Data encountered in solving problems often do not fall exactly on the grid of values provided by property tables, and linear interpolation between adjacent table entries becomes very necessary. Interpolation can be single linear interpolation or double linear interpolation.
The example below illustrates the principles applied in single linear and double linear interpolation.
The following table lists temperatures and specific volumes of water vapour at two pressures:
Using the data provided here, estimate
(a) The specific volume at T= 240°C, p = 1.25 MPa, in m3/kg.
(b) The temperature at p = 1.5 MPa, v = 0.1555 m3 /kg, in °C.
(c) The specific volume at T = 220°C, p = 1.4 MPa, in m3/kg
SOLUTION
(a) At the temperature of 240 0C, the specified pressure of 1.25 MPa falls between the table values of 1.0 MPa and 1.50 MPa. To determine the specific volume corresponding to 1.25 MPa, we think of the slope of a straight line joining the adjacent states as follows:

## Slide 25: Basic Concepts and Definitions
INTERPOLATION
Similar triangles (Negative Slope):
(b) At a pressure of 1.5 MPa, the given specific volume of 0.1555 m3/kg falls between the table values of 240 0C and 280 0C. To determine the temperature corresponding to the given specific volume, we think of the slope of a line joining the adjacent table states, as follows:
Similar triangles (Positive Slope):
(c) In this case, the specified pressure falls between the table values of 1.0 MPa and 1.5 MPa and the specified temperature also falls between the table values of 200 0C and 240 0C.
Thus, double interpolation is required.

## Slide 26: Basic Concepts and Definitions
INTERPOLATION
At 220 0C, the specific volume at each pressure is simply the over the interval since 220 0C falls midway between 200 0C and 240 0C.
At 1.0 MPa, 220 0C; v = (0.2060 + 0.2275)/2 = 0.21675 m3/kg
At 1.5 MPa, 220 0C; v = (0.1325 + 0.1483)/2 =0.1404 m3/kg
Thus with same approach as in (a), we write as follows

## Slide 27: Basic Concepts and Definitions
Thermodynamic State
The word state refers to the condition of a system as described by its properties.
The state can be specified by at least two thermodynamic properties.
Thermodynamic Process
When any of the properties of a system change the state changes and the system is said to have undergone a process.
A process is a transformation from one thermodynamic state to another.
If a system exhibits the same values of its properties at two different times, it is in the same state at those times.
A system is said to be at steady state if none of its properties change with time.

## Slide 28: Basic Concepts and Definitions
Path of a process
The series of states through which a system passes during a process is called the path of the process.
To describe a process completely, one should specify the initial and final states of the process, as well as the path it follows, and the interaction with the surroundings.
An isothermal process occurs at constant temperature.
An isobaric process is at constant pressure.
An isochoric process is at constant volume.

## Slide 29: Basic Concepts and Definitions
Point Functions
The value of a property of a system is independent of the path of the process undergone by the system.
It is therefore referred to as a point or state function.
The change in the value of a state function depends solely on its values at the initial and final states and not on the path.
Path Functions
Quantities such as heat and work are not properties of the system and therefore depends on the path of the process undergone by the system.
Hence, they are referred to as path functions.
The change in value of a path function depends on the path of the process.
They are symbolized using inexact differential such as δQ (for heat) and δW (for work)

## Slide 30: Basic Concepts and Definitions
Thermodynamic cycle
A thermodynamic cycle is a sequence of processes that begins and ends at the same state.
In a cycle, the net change in value of any property is equal to zero.
Cycles that are repeated periodically play prominent roles in many areas of application. For example, steam circulating through an electrical power plant executes a cycle.
Thermodynamic Equilibrium
A system is in thermodynamic equilibrium with its surroundings if no further changes occur in its properties:
3 conditions are satisfied:
mechanical equilibrium: forces are balanced.
thermal equilibrium: temperature is uniform.
chemical equilibrium: no change in composition and no transfer of matter.

## Slide 31: Basic Concepts and Definitions
Quasi-Static Process
A process is said to be quasi-static if it proceeds in such a manner that, at any instance, the system is only infinitesimally displaced from the equilibrium with the surroundings.
A quasi-static process implies the system is essentially in internal equilibrium so that the properties are uniform.
Adiabatic Process
A process during which there is no heat transfer is called an adiabatic process.
There are two ways a process can be adiabatic.
Thermal insulation or system having same temperature with surroundings.

## Slide 32: Basic Concepts and Definitions
Reversible Process
A process is said to be reversible if after it has been carried out it is possible by any means whatsoever to restore the system and surroundings to exactly the same initial states as before.
Since thermodynamics deals only with systems in equilibrium, it follows that it deals necessarily with reversible processes.
In practice, the reversible process represents the optimum path for all energy conversion processes.
A good example of reversible processes is the evaporation of liquid in which temperature and pressure remains essentially the same throughout the processes.
The process path is indicated by a solid line.

## Slide 33: Basic Concepts and Definitions
Irreversible Process
If the system departs significantly from equilibrium during the process, both internally and externally, the process is irreversible.
The direction of such a process cannot be interchanged because of the differences in the values of properties within the system and also between the system and surroundings.
Irreversible processes include doing work against friction, unrestrained expansion, mixing of two fluids, heat transfer across a finite temperature difference, inelastic deformation of solids, chemical reactions and the transfer of current against electrical resistance.
Process path is represented by broken lines.
Unrestrained expansion of a gas

## Slide 34: Basic Concepts and Definitions
Energy, Heat and Work
Energy is simply defined as the capacity to do work or supply heat.
Heat and work are transient forms of energy which appear only at the boundary of systems.
Heat is energy flow by virtue of a temperature difference. Heat is not contained in a system. Heat only exists as energy crossing the boundary.
A distinction is made between thermal energy and heat. Thermal energy is part of the internal energy, hence contained in the system. Heat is thermal energy crossing the boundary.
Work is defined in mechanics as the product of force and distance, measured in the direction of application of the force.
Note: Work, like heat, is energy in transit and not a property of a system.
There are many forms: electrical, magnetic, chemical and mechanical work (including work due to expansion and compression).

## Slide 35: Basic Concepts and Definitions
Internal Energy, U
Internal Energy is the energy associated with the microscopic components of the system.
It includes the kinetic and potential energy associated with the random motion (rotational, vibration and translation) of the atoms and molecules.
Also includes potential energy bonding the particles together.
Note
It does not include the macroscopic kinetic energy or external potential energy.

## Slide 36: Basic Concepts and Definitions
Flow Energy
Flow energy is considered the energy contained in the flowing fluid.
This is considered to be different from internal energy in thermodynamics.
It is expressed as product of pressure and volume of the fluid.
The total energy associated with any thermodynamic system is equal to its internal energy plus macroscopic kinetic energy, external potential energy and the flow energy of the fluid.
E = U + KE + PE + (PV)FE

## Slide 37: Basic Concepts and Definitions
Simple Compressible System
The term simple system is applied when there is only one form of work (either mechanical, or electrical, or magnetic, or chemical) as the system undergoes a quasi-static process.
When expansion or compression is the only mode of work transfer, the system is said to be a simple compressible system.
The boundary work due to expansion or compression is expressed as;
δW = PdV

## Slide 38: Basic Concepts and Definitions
Simple Compressible System
The boundary work due to expansion or compression is expressed as;
δW = PdV
PdV work is commonly encountered in reciprocating devices such as automotive engines and compressors.

## Slide 39
KNUST-SESC