## Slide 1: THERMODYNAMICS I (ME 265)
Francis Kofi Forson (Professor)
Department of Mechanical Engineering
Kwame Nkrumah University of Science and Technology, Kumasi, Ghana
INTRODUCTION
(Basic Concepts and Definitions)

## Slide 2: Introduction
Thermodynamics is concerned with the study of energy, its forms and transformations, and the interactions of energy with matter.
Thermodynamics is both a branch of physics and an engineering science.
Engineers are generally interested in studying systems and how they interact with their surroundings. To facilitate this, engineers extend the subject of thermodynamics to the study of systems through which matter flows.
What is thermodynamics?

## Slide 3: Introduction
Systems may be studied from the macroscopic or microscopic approach.
The macroscopic approach to thermodynamics is concerned with the gross or overall behaviour. This is sometimes called classical thermodynamics.
The microscopic approach, is concerned directly with the structure of matter. It is known as statistical thermodynamics.
The macroscopic viewpoint is what is generally adopted in engineering thermodynamics but for understanding concepts are interpreted from the microscopic viewpoint.
Two Approaches to Thermodynamics

## Slide 4: Introduction
Four laws of thermodynamics are:
Zeroth law
First law
Second law
Third law
The state postulate
  Laws of Thermodynamics

## Slide 5: Zeroth Law of Thermodynamics
If Body A has same temperature as body C and body B has same temperature as C, then A and B have the same temperature. This forms the basis for comparison of temperatures.
The Zeroth Law states that, if two systems are in thermal equilibrium with a third system, then the two systems are equally in thermal equilibrium with each other.
The third body or system is usually a thermometer.
A
B
C

## Slide 6: First Law of Thermodynamics
It obeys the conservation of energy which states that energy can neither be created nor destroyed but can be transformed from one form to other.
If a system does not interact with its environment in any way then no energy comes in and no energy goes out. Energy is “conserved”.
There is always an energy balance.

## Slide 7: Second Law of Thermodynamics
Aspects of Second Law include;
Predicting the direction of processes.
Establishing conditions for equilibrium. determining the best theoretical performance of cycles, engines, and other devices.
Evaluating quantitatively the factors that preclude attainment of the best theoretical performance level.

## Slide 8: Third Law of Thermodynamics
It states that, it is impossible to attain a temperature of absolute zero.
On the Kelvin temperature scale, T = 0K is often referred to as absolute zero.
If absolute zero temperature (0K) can be obtained, 100% efficiency can be achieved.

## Slide 9: Applications of Thermodynamics

## Slide 10: Basic Concepts and Definitions
Thermodynamic system is a region of space or an amount of matter, bounded by an arbitrary surface.
Everything external to the system is considered to be part of the system’s surroundings.
The system is distinguished from its surroundings by a specified boundary, which may be at rest or in motion.
A boundary is a closed surface, either real or imaginary, surrounding a system through which energy and mass may enter or leave the system and which separates the system from its surroundings.
Permeable and process boundaries allow mass transfer to occur.
A diathermal boundary allows heat transfer to occur across it as in the case of thin metal walls.

## Slide 11: Basic Concepts and Definitions
Once the system is defined and the relevant interactions with other systems are identified, one or more physical laws or relations are applied.
The system is whatever we want to study. We may want to study a quantity of matter contained within a closed, rigid-tank, or we may want to consider something such as a gas pipeline through which matter flows.
Note:
Even vacuum which is devoid of matter, may be the focus of interest. The composition of matter inside a system may be fixed or may be changing through chemical or nuclear reactions. The shape or volume of the system being analysed is not necessarily constant, as when a piston compresses a gas in a cylinder or a balloon is being inflated.

## Slide 12: Basic Concepts and Definitions
Classification of Systems
A thermodynamic system interacts with its surroundings through its boundary in two ways: by exchanging energy and matter (mass).
Types of systems
Closed system.
Open system
Isolated system

## Slide 13: Basic Concepts and Definitions
Sign Convention
Energy interaction occurs in two ways; heat and work.

## Slide 14: Basic Concepts and Definitions
Thermodynamic Properties
A property is a characteristic of a system. It is used to specify the condition of that system.
The most common properties are pressure, temperature, mass, volume and energy.
A property must be macroscopic, measurable and have a single numerical value that does not depend on how the condition of the system was attained.
Thermodynamic properties are classified as Intensive and Extensive properties.
Extensive properties depend on the extent or size of the system and hence vary directly with the mass. Examples are mass, volume, energy.
Intensive properties are independent of the size of the system. Examples are Pressure, and temperature.
Specific properties (denoted by lower case letters) are defined as the value of an extensive property per unit mass. They are therefore, independent of mass and are regarded as intensive properties.

## Slide 15: Basic Concepts and Definitions
Thermodynamic State
The word state refers to the condition of a system as described by its properties.
The state can be specified by at least two thermodynamic properties.
Thermodynamic Process
When any of the properties of a system change the state changes and the system is said to have undergone a process.
A process is a transformation from one thermodynamic state to another.
If a system exhibits the same values of its properties at two different times, it is in the same state at those times.
A system is said to be at steady state if none of its properties change with time.

## Slide 16: Basic Concepts and Definitions
Path of a process
The series of states through which a system passes during a process is called the path of the process.
To describe a process completely, one should specify the initial and final states of the process, as well as the path it follows, and the interaction with the surroundings.
An isothermal process occurs at constant temperature.
An isobaric process is at constant pressure.
An isochoric process is at constant volume.

## Slide 17: Basic Concepts and Definitions
Point Functions
The value of a property of a system is independent of the path of the process undergone by the system.
It is therefore referred to as a point or state function.
The change in the value of a state function depends solely on its values at the initial and final states and not on the path.
Path Functions
Quantities such as heat and work are not properties of the system and therefore depends on the path of the process undergone by the system.
Hence, they are referred to as path functions.
The change in value of a path function depends on the path of the process.
They are symbolized using inexact differential such as δQ (for heat) and δW (for work)

## Slide 18: Basic Concepts and Definitions
Thermodynamic cycle
A thermodynamic cycle is a sequence of processes that begins and ends at the same state.
In a cycle, the net change in value of any property is equal to zero.
Cycles that are repeated periodically play prominent roles in many areas of application. For example, steam circulating through an electrical power plant executes a cycle.
Thermodynamic Equilibrium
A system is in thermodynamic equilibrium with its surroundings if no further changes occur in its properties:
3 conditions are satisfied:
mechanical equilibrium: forces are balanced.
thermal equilibrium: temperature is uniform.
chemical equilibrium: no change in composition and no transfer of matter.

## Slide 19: Basic Concepts and Definitions
Quasi-Static Process
A process is said to be quasi-static if it proceeds in such a manner that, at any instance, the system is only infinitesimally displaced from the equilibrium with the surroundings.
A quasi-static process implies the system is essentially in internal equilibrium so that the properties are uniform.
Adiabatic Process
A process during which there is no heat transfer is called an adiabatic process.
There are two ways a process can be adiabatic.
Thermal insulation or system having same temperature with surroundings.

## Slide 20: Basic Concepts and Definitions
Reversible Process
A process is said to be reversible if after it has been carried out it is possible by any means whatsoever to restore the system and surroundings to exactly the same initial states as before.
Since thermodynamics deals only with systems in equilibrium, it follows that it deals necessarily with reversible processes.
In practice, the reversible process represents the optimum path for all energy conversion processes.
A good example of reversible processes is the evaporation of liquid in which temperature and pressure remains essentially the same throughout the processes.
The process path is indicated by a solid line.

## Slide 21: Basic Concepts and Definitions
Irreversible Process
If the system departs significantly from equilibrium during the process, both internally and externally, the process is irreversible.
The direction of such a process cannot be interchanged because of the differences in the values of properties within the system and also between the system and surroundings.
Irreversible processes include doing work against friction, unrestrained expansion, mixing of two fluids, heat transfer across a finite temperature difference, inelastic deformation of solids, chemical reactions and the transfer of current against electrical resistance.
Process path is represented by broken lines.
Unrestrained expansion of a gas

## Slide 22: Basic Concepts and Definitions
Energy, Heat and Work
Energy is simply defined as the capacity to do work or supply heat.
Heat and work are transient forms of energy which appear only at the boundary of systems.
Heat is energy flow by virtue of a temperature difference. Heat is not contained in a system. Heat only exists as energy crossing the boundary.
A distinction is made between thermal energy and heat. Thermal energy is part of the internal energy, hence contained in the system. Heat is thermal energy crossing the boundary.
Work is defined in mechanics as the product of force and distance, measured in the direction of application of the force.
Note: Work, like heat, is energy in transit and not a property of a system.
There are many forms: electrical, magnetic, chemical and mechanical work (including work due to expansion and compression).

## Slide 23: Basic Concepts and Definitions
Internal Energy, U
Internal Energy is the energy associated with the microscopic components of the system.
It includes the kinetic and potential energy associated with the random motion (rotational, vibration and translation) of the atoms and molecules.
Also includes potential energy bonding the particles together.
Note
It does not include the macroscopic kinetic energy or external potential energy.

## Slide 24: Basic Concepts and Definitions
Flow Energy
Flow energy is considered the energy contained in the flowing fluid.
This is considered to be different from internal energy in thermodynamics.
It is expressed as product of pressure and volume of the fluid.
The total energy associated with any thermodynamic system is equal to its internal energy plus macroscopic kinetic energy, external potential energy and the flow energy of the fluid.
E = U + KE + PE + (PV)FE

## Slide 25: Basic Concepts and Definitions
Simple Compressible System
The term simple system is applied when there is only one form of work (either mechanical, or electrical, or magnetic, or chemical) as the system undergoes a quasi-static process.
When expansion or compression is the only mode of work transfer, the system is said to be a simple compressible system.
The boundary work due to expansion or compression is expressed as;
δW = PdV

## Slide 26: Basic Concepts and Definitions
Simple Compressible System
The boundary work due to expansion or compression is expressed as;
δW = PdV
PdV work is commonly encountered in reciprocating devices such as automotive engines and compressors.

## Slide 27
KNUST-SESC