## Slide 1: THERMODYNAMICS I (ME 265)
Francis Kofi Forson (PhD)
Department of Mechanical Engineering
Kwame Nkrumah University of Science and Technology, Kumasi, Ghana
SECOND LAW OF THERMODYNAMICS

## Slide 2: Second Law of Thermodynamics
A process will occur in a specified direction, not just in any direction:
Water flows down a water fall
Impossible
Heat flow from a high temperature to a low temperature
HIGH Temperature
LOW Temperature
Impossible

## Slide 3: Second Law of Thermodynamics
A Process will occur in a specific direction, not just in any direction:
Gas expands from a high pressure to a low pressure
Heat is generated when current flows
HIGH
Pressure
LOW Pressure
Impossible
Heat generation

## Slide 4: Second Law of Thermodynamics
Thermal Energy Reservoir (Heat Reservoir)
It is a hypothetical body with a relatively large thermal energy (heat) capacity that can supply or absorb finite amounts of heat without undergoing any change in temperature.
The only significant property of a heat reservoir is that its temperature must remain constant so that any processes that take place in the reservoir must be reversible.
A reservoir that supplies energy in the form of heat is called a source, and one that absorbs energy in the form of heat is called a sink.

## Slide 5: Second Law of Thermodynamics
Thermal Energy Reservoir (Heat Reservoir)
Atmosphere
Ocean
Rivers
Examples of Sink

## Slide 6: Second Law of Thermodynamics
Thermal Energy Reservoir (Heat Reservoir)
Examples of Sources
Boiler furnace
Nuclear reactor
Sun

## Slide 7: Second Law of Thermodynamics
Heat Engine
It is a closed system which operates in a cycle and produces a net quantity of work from a supply of heat.
WORK
HEAT
NATURE
directly and completely (100%)
HEAT
WORK
NEED A HEAT ENGINE
(No 100% conversion)
NO 100 % CONVERSION OF HEAT TO WORK
(NO 100 % THERMAL EFFICIENCY)

## Slide 8: Second Law of Thermodynamics
Heat Engine:
4 Conditions for the working fluid
It receives heat from a high-temperature source (solar energy, oil furnace, nuclear reactor, etc.)
It converts part of this heat into work (usually in the form of a rotating shaft)
It rejects the remaining heat into a low-temperature sink (the atmosphere, rivers, etc.)
It goes through a thermodynamic cycle.
High Temperature source
Low Temperature sink
Heat Engine
Qin
Qout
Wout
400 MW
160 MW
240 MW

## Slide 9: Second Law of Thermodynamics
Heat Engine:
Some examples of heat engines are;
Steam power plants
Gas power plants
Automobile engines
Boiler
Condenser
Turbine
Pump
Turbine
Qin
Qout
Wout
Win
400 MW
165 MW
240 MW
5 MW

## Slide 10: Second Law of Thermodynamics
Thermal Efficiency of a Heat Engine:
Boiler
Condenser
Turbine
Pump
Turbine
Qin
Qout
Wout
Win
400 MW
165 MW
240 MW
5 MW
= = 40%

## Slide 11: Second Law of Thermodynamics
Kelvin-Planck statement of the Second Law:
It is impossible for any device that operates on a cycle to receive heat from a reservoir and do an equivalent amount of work on the surroundings.
There is no heat engine with 100 % thermal efficiency.
High Temperature source
Heat Engine
Qin
Wnet out
400 MW
400 MW
Impossible (PMM 2nd kind)

## Slide 12: Second Law of Thermodynamics
Heat Engine: Example 1
Heat is transferred to a heat engine from a furnace at a rate of 80 MW. If the rate of waste heat rejection to a nearby river is 50 MW, determine the net power output and the thermal efficiency for this heat engine.
= Qnet = 80 MW – 50 MW = 30 MW
= = 37.5%

## Slide 13: Second Law of Thermodynamics
Heat Engine: Example 2
A steam power plant is constructed such that it produces 75 kW of power while rejecting 190 kW of heat to a low-temperature reservoir.
Determine the rate of heat supplied
Determine the thermal efficiency.
Suggested Answers:
[ 265 kW; 28.3%]
Heat Engine: Example 3
An engine receives heat at the rate of 2000 kJ/min and produces 10 kW of power at the output shaft. Determine the efficiency and the heat rejected per minute.
Suggested Answers:
[ 30%; 1400 kJ/min]

## Slide 14: Second Law of Thermodynamics
Reversed Heat Engine:
It is a closed system which operates in a cycle such that it extracts heat from a low-temperature reservoir and rejects heat to a high temperature reservoir while a net quantity of work is done on the system by the surroundings.
Refrigerators and Heat pumps are examples of reversed heat engines.
High Temperature source TH
Low Temperature sink TL
Impossible

## Slide 15: Second Law of Thermodynamics
Reversed Heat Engine:
If the desired effect is the heat extracted from the low temperature sink (QL), the system is referred to as a refrigerator.
If the desired effect is the heat rejected to the high temperature source (QH), the system is referred to as a heat pump.
High Temperature source TH
Low Temperature sink TL
RHE
Win
QH
QL
QH
QL
QH
QL
Condition

## Slide 16: Second Law of Thermodynamics
Performance of Refrigerators and Heat pumps
Coefficient of performance
Compressor
Condenser
Evaporator
Expansion device

## Slide 17: Second Law of Thermodynamics
Clausius statement of the Second Law:
It is impossible to construct a system that operates in a cycle and transfer heat from a cooler to a hotter body without work being done on the system by the surroundings.
  Win = 0 kW
in= ⇒ COP
Environment at TH
Area to cool at TL
Refrig
QH
QL
  25 kW
  25 kW

## Slide 18: Second Law of Thermodynamics
Reversed Heat Engine: Example 1
The food compartment of a refrigerator is removing heat at a rate of 360 kJ/min. if the required power input to the refrigerator is 2 kW, determine the COP of the refrigerator and the rate of heat rejection to the room that houses the refrigerator. What would be the COP of a corresponding heat pump?
Suggested Answers: [ 3; 8 kW; 4]
Reversed Heat Engine: Example 2
A household refrigerator with a COP of 1.8 removes heat from the refrigerated space at a rate of 90 kJ/min. Determine
a) the electric power consumed by the refrigerator in kW and
b) the rate of heat transfer to the kitchen air in kJ/min
Suggested Answers: [ 0.83 kW; 140 kJ/min]

## Slide 19: Second Law of Thermodynamics
Reversed Heat Engine: Example 3
An air conditioner removes heat steadily from a house at a rate of 750 kJ/min while drawing electric power at a rate of 5 kW. Determine
a) the COP of this air conditioner and
b) the rate of heat transfer to the outside air in kJ/min.
Suggested Answers: [ 2.5; 1050 kJ/min]
Reversed Heat Engine: Example 4
Determine the COP of a heat pump that supplies energy to a house at a rate of 8000 kJ/h for each kW of electric power it draws. Also determine the rate of energy absorption from the outside air in kJ/h.
Suggested Answers: [ 2.22; 4400 kJ/h]

## Slide 20: Second Law of Thermodynamics
Note:
Every system operating in a cycle must satisfy both the first law and second law
Boiler
Condenser
Turbine
Pump
Turbine
Qin
Qout
Wout
Win
400 MW
405 MW
0 MW
5 MW
Satisfies First Law
Violates Second Law

## Slide 21: Second Law of Thermodynamics
Note:
Every system operating in a cycle must satisfy both the first law and second law
Boiler
Condenser
Turbine
Pump
Turbine
Qin
Qout
Wout
Win
400 MW
165 MW
200 MW
5 MW
Satisfies Second Law
Violates First Law

## Slide 22: Second Law of Thermodynamics
Note:
Every system operating in a cycle must satisfy both the first law and second law
Boiler
Condenser
Turbine
Pump
Turbine
Qin
Qout
Wout
Win
400 MW
165 MW
240 MW
5 MW
Satisfies Second Law
Satisfies First Law

## Slide 23: Second Law of Thermodynamics
Reversibility
A process undergoes a change in a particular direction.
If the process can be reversed in such a manner that the path can be exactly traced to restore the system and its surroundings to their original state, then the process is said to be reversible.
A reversible process is an idealization of actual processes.
They are easy to analyze and serve as a yardstick which actual processes can be compared to.
Conditions for reversibility
The process may proceed in either direction.
That the system is always in a state of equilibrium.
Heat energy transfer process is isothermal.
That friction is absent.
The energy transformations in both directions must be equal.
That the system and its surroundings can be restored to its original condition by retracing in the reverse direction every point it took in the original direction.

## Slide 24: Second Law of Thermodynamics
Irreversibility
If the process cannot be reversed in such a manner that the path can be exactly traced to restore the system and its surroundings to their original state, then the process is said to be irreversible.
Actual processes encounter some irreversibilities.
Conditions for irreversibility
The presence of friction
Heat energy transfer from a higher to a lower temperature.
Unrestricted expansion (or free expansion) from a higher to a lower pressure.
Paddle or stirring wheel work
Lack of pressure equilibrium throughout the system.
Presence of electrical resistance.

## Slide 25: Second Law of Thermodynamics
Heat Engine Cycle
Steam power plant

## Slide 26: Second Law of Thermodynamics
Carnot Principle
Sadi Carnot proposed a heat engine cycle composed of reversible processes which gave maximum possible net work output when operating between two fixed temperature limits, TC and TH.
By definition, the only significant property of a heat reservoir is its temperature, not its substance.
Between the same two reservoirs, the efficiency of a reversible heat engine is always greater than the efficiency of an irreversible one.

## Slide 27: Second Law of Thermodynamics
Carnot Efficiency
Carnot efficiency is the theoretical maximum efficiency that only a reversible heat engine (HE) operating between the temperature limits, TH and TC can achieve.
Example: What is the Carnot efficiency of a Heat engine operating between a heat source of 1000 K and a heat sink of 300 K?

## Slide 28: Second Law of Thermodynamics
SOURCE @ TH = 1000 K
SINK @ TC = 300 K
ImpossibleHE
th > 70%
ReversibleHE
th = 70%
IrreversibleHE
th< 70%

## Slide 29: Second Law of Thermodynamics
Heat Engine on Carnot Principle: Example 1
A power cycle operating between two reservoirs receives energy QH by heat transfer from a hot reservoir at TH = 2000K and rejects energy QC by heat transfer to a cold reservoir at TC = 400K. For each of the following cases, determine whether the cycle operates reversibly, irreversibly, or is impossible.
QH = 1000 kJ, Wnet = 850 kJ b) QH = 2000 kJ, QC = 400 kJ
c) Wnet = 1600 kJ, QC = 500 kJ d) QH = 1000 kJ, η = 30%
Suggested answers [(a) impossible; (b) reversible; (c) irreversible; (d) irreversible

## Slide 30: Second Law of Thermodynamics
Carnot Heat Engine: Example 2
A Carnot heat engine receives 500 kJ of heat from a source of unknown temperature and rejects 200 kJ of it to a sink at 17 °C. Determine
a) the temperature of the source and
b) the thermal efficiency of the heat engine.
Suggested Answers: [452 °C; 60%]
Carnot Heat Engine: Example 3
An engine operates on the Carnot cycle. The engine efficiency is 60 percent when 20 kJ/kg per engine cycle of thermal energy is rejected to a low-temperature reservoir at TC = 27 °C, and has a specific net work output of magnitude 30 kJ/kg per cycle.
(a) How much energy is transferred to the engine from the high-temperature reservoir per cycle (kJ/kg)?
(b) At what temperature TH is the high-temperature reservoir?
Suggested Answers: [50 kJ/kg; 477 °C]

## Slide 31: Second Law of Thermodynamics
Reversed Heat Engine on Carnot Principle: Example 1
A refrigeration cycle operating between two reservoirs receives energy QC from a cold reservoir at TC = 250 K and rejects energy QH to a hot reservoir at TH = 300 K. For each of the following cases, determine whether the cycle operates reversibly, irreversibly, or is impossible.
QC = 1000 kJ, Win = 400 kJ b) QC = 2000 kJ, Win = 2200 kJ
c) Win = 500 kJ, QH = 3000 kJ d) Win = 1000 kJ, COPR = 6
Suggested answers [(a) irreversible; (b) irreversible; (c) reversible; (d) impossible

## Slide 32: Second Law of Thermodynamics
Reversed Carnot Heat Engine: Example 2
A Carnot heat pump delivers a heat transfer of 3 x 104 kJ at 50 °C. The evaporator is at 15 °C. Calculate the power input and the coefficient of performance for this Carnot heat pump.
Suggested Answers: [3.25 x 103 J; 9.229]
Reversed Carnot Heat Engine: Example 3
A Carnot refrigerator rejects a heat transfer of 2.5 x 103 kJ at 80 °C. If the power input for this refrigerator is 1.1 x 103 kJ, find the heat transferred, the low temperature in the cycle, and the coefficient of performance.
Suggested Answers: [1.4 x 103 kJ; -75.3 °C; 1.27 ]

## Slide 33: Second Law of Thermodynamics
Entropy
Entropy is a quantitative measure of the disorderliness or randomness of a system.
It is a measure of energy that is no longer available to perform useful work within the current environment.
Second Law: There exist a property of a closed system such that a change in its value is greater than or equal to the heat transfer to the system over some constant temperature.
This property is called Entropy (S).
This law is expressed mathematically as;
For a reversible process
For an irreversible process
Sgen is the entropy generation within the system itself as a result of friction and other irreversibilities present within the system.

## Slide 34: Second Law of Thermodynamics
Entropy
For a reversible adiabatic process, the entropy of the system during the process remains constant. Thus, the entropy change of the system during the process is zero (dS = 0).
The entropy change of an isolated system during a process always increases or in the limiting case of a reversible process remains constant.
S
T
1
2
Constant entropy process (isentropic process)
Q12 = 0
Q12
S
T
1
2
Constant temperature process (isothermal process)

## Slide 35: Second Law of Thermodynamics
Entropy
∆S is a measure of the level of irreversibilities in the system.
Isentropic efficiency: a comparison of performance between ideal and actual work producing devices.
Fluid
Blades
Turbines
Energy

## Slide 36: Second Law of Thermodynamics
Entropy
∆S is a measure of the level of irreversibilities in the system.
Isentropic efficiency: a comparison of performance between ideal and actual work consuming devices.
Fluid
Blades
Pumps
Compressors
Fans
Energy

## Slide 37: Second Law of Thermodynamics
Entropy
∆S is a measure of the level of irreversibilities in the system.
Isentropic efficiency: a comparison of performance between ideal and actual work producing or consuming devices.
Example: = 90% and Wisen = 250 MW
Wactual = 250 x 0.9 = 225 MW
Example: = 95% and Wisen = 100 MW
Wactual = 100 / 0.95 = 105 MW

## Slide 38: CLAUSSIUS INEQUALITY
≤ 0
Entropy change of the universe
= 0

## Slide 39: Second Law of Thermodynamics
Carnot Cycle: Four processes
Two isothermal (constant temperature) heat transfer processes
Two reversible adiabatic (constant entropy) work transfer processes
S
T
1
4
2
3
Qnet = Wnet
TH
TC

## Slide 40: Second Law of Thermodynamics
Reversed Carnot Cycle: Being a reversible cycle, all the processes that comprise the Carnot cycle can be reversed, in which case it becomes the Carnot refrigeration cycle or Carnot heat pump cycle.
S
T
4
1
3
2
Qnet = Wnet
TH
TC

## Slide 41: Second Law of Thermodynamics
Example:
A fridge working on the reversed Carnot cycle has a power requirement of 5 kW. If the maximum and minimum temperatures in the cycle are 40 °C and -10 °C respectively, determine:
(a) The COP
(b) The rate of heat extraction from the cold space
(c) The change in specific entropy for each of the processes in the cycle, given a refrigerant mass flow rate of 0.32 kg/s
S
T
4
1
3
2
Qnet = Wnet
TH
TC
Solution:

## Slide 42: Second Law of Thermodynamics
Solution
S
T
4
1
3
2
Qnet = Wnet
TH
TC

## Slide 43: Second Law of Thermodynamics
Note
S3 – S2 =0 and S1 – S4 =0
≤ 0
= 0 when all processes are reversible in the cycle
< 0 when there are irreversibilities

## Slide 44: Second Law of Thermodynamics
Example 2
A system of 100 kg mass undergoes a process in which the specific entropy increases from 0.3 kJ/(kg.K) to 0.4 kJ/(kg. K). At the same time, the entropy of the surroundings of the system decreases from 80 kJ/K to 75 kJ/K. This process is:
(a) reversible (b) irreversible (c)reversible and adiabatic (d) impossible

## Slide 45: Second Law of Thermodynamics
Solution
The total entropy change of the universe never decreases during a process undergone by a system.
That is ∆Stotal = ∆Ssystem + ∆Ssurroundings
∆Ssystem= m∆ssystem= m(sf-si) = 100 kg (0.4 – 0.3)kJ/K = +10 kJ/K
∆Ssurroundings= (75 -80) kJ/K = -5 kJ/K
∆Stotal = +10 kJ/K -5 kJ/K = +5 kJ/K > 0
It implies that the process undergone by the system is irreversible

## Slide 46
KNUST-SESC