## Slide 1: TUTORIALS
ME 282

## Slide 2: QUESTION 1
Compute the strain-hardening exponent n for an alloy in which a true stress of 415 MPa produces a true strain of 0.10; assume a value of 1035 MPa for K.

## Slide 3: QUESTION 2
For a brass alloy, the stress at which plastic deformation begins is 345 MPa, and the modulus of elasticity is 103 GPa.
(a) What is the maximum load that can be applied to a specimen with a cross-sectional area of 130 mm2 without plastic deformation?

## Slide 4: QUESTION 3
Consider a cylindrical nickel wire 2.0 mm (0.08 in.) in diameter and 104 mm (1200 in.) long. Calculate its elongation when a load of 300 N is applied. Assume that the deformation is totally elastic with modulus 207GPa.

## Slide 5: QUESTION 4
A cylindrical specimen of steel having an original diameter of 12.8 mm is tensile tested to fracture and found to have an engineering fracture strength sf of 460 MPa. If its cross-sectional diameter at fracture is 10.7 mm, determine
The ductility in terms of percentage reduction in area
The true stress at fracture