## Slide 1: AE 460 MAINTENANCE AND REPAIRS
J. K. AFRIYIE

## Slide 2: COURSE OUTLINE
Definitions.
Concepts of planned maintenance, Decisions relating to maintenance, Planning and organising the maintenance and repair functions.
Manufacturing and repair accuracy, Repair materials. Basic repair operation. Replacement parts supply and management. Workshop safety.

## Slide 3: ADDITIONAL TOPICS
Repairs & Maintenance processes
Diagnosis
Clean and washing
Disassembling
Inspection
Repairing and servicing
Re-assembling and testing
Types of wear
Lubrication
Survey of Workshop Handtools and Machine Tools
Methods of joining metals: (Basic workshop operations) riveting, welding, bolting, soldering and brazing
Machinery maintenance: (implementation on farm and large organisation, basic maintenance decisions including concepts of preventive and failure maintenance
Use of internal and external service personnel
Contract vrs incident negotiations for external service, etc
Spare parts procurement and stocking, etc

## Slide 4: REFERENCES
Internet
Principles of Planned Maintenance
  R. H. Clifton
  ISBN: 0 7131 3317 1
  Edward Arnold (Publications) Ltd.
Agricultural Mechanics; Fundamentals & Applications; 2nd edition
  Elmer L. Cooper, Ed.D.
  H. Edward Reiley, Consulting Editor
  Delmar Publishers Inc.

## Slide 5: GENERAL INTRODUCTION
Well maintained machinery = Lynch pin of successful farm business
  Breakdowns cost time and money in the idle time waiting for repairs
    Time spent waiting for dealer or mechanics to arrive
    Time and cost of purchase of spare parts
  Modern plant & equipment require heavy capital expenditure, making downtime extremely costly
Regular maintenance helps to avoid the above scenarios
Regular maintenance enables manufacturing plants to operate efficiently and accurately at the required level of production
It helps to reduce or stabilise manufacturing costs

## Slide 6: GENERAL INTRODUCTION (contd.)
Hidden costs lie in lost opportunities, e.g.
  Grain could not be harvested because the combine harvester was laid up during two (2) fine days before the deluge (sudden heavy downpour, great flood, an overwhelming amount).
  The silage crop (for animal fodder) was left down to dry because the forage harvester was out of commission.
  The seed should have been sown two weeks ago but this could not be because the drill was defunct.
  Frequent breakdowns of the refuse track did not allow effective disposal of refuse. This led to the spread of pests and diseases.

## Slide 7: GENERAL INTRODUCTION (contd.)
The above scenarios and some other problems at times crop up.
  Therefore, many efficient Units maintain a farm workshop with a capacity for on-the-spot machinery repairs (well-equipped workshop and experienced fitters/mechanics ) to keep the downtime to a minimum.

## Slide 8: MAINTENANCE
Maintenance is the act of keeping fixed assets in an acceptably functioning condition.
Maintenance has become more important than ever, due to
  The emergence of complex modern machines
  The need to adhere to very tight planning for operations
It includes
  Preventive maintenance
  Repairs
  Cyclical maintenance (component replacement)
  Activities to address the statutory requirements needed for the asset to achieve its expected life
It excludes
  Upgrade activities aimed at expanding the capacity
  Activities for changing the function of the asset

## Slide 9: MAINTENANCE (contd.)
Maintenance is an indispensable part of a production system
Prime Objective of maintenance
  To ensure availability of existing plant, equipment and buildings in a manner required for efficient operation of the farm

## Slide 10: MAINTENANCE (contd.)
Maintenance must be carefully planned in conjunction with
  the operational requirements
  schedules of the farm (or the manufacturing company)
It must, however, be planned such that it does not obscure the real objectives of the farm or become a ‘tail wagging the dog’

## Slide 11: PRINCIPLES OF MAINTENANCE
Maintenance is best performed at a level that is
  Best qualified
  Responsive
  Cost effective
Repairs beyond organic capability (at natural level of the organisation), delivered to the next level
Unit performance before evacuated
Controlled exchange, used to support maintenance

## Slide 12: ANNUAL MAINTENANCE (AM)
Work performed to maintain serviceability or repair of failures in the year in which they occur
Includes preventive and cyclic maintenance
Can be
  scheduled (planned)
  unscheduled (unplanned), out of catastrophic failures
An estimation for this is allowed in reputable organisations by raising the Current Replacement Value by 3-5%

## Slide 13: PREVENTIVE MAINTENANCE (PM)
Scheduled (planned) servicing, repairs, inspections and replacement of parts
It results in fewer breakdowns & fewer premature replacements of parts
It helps to achieve the expected life of the fixed asset
Regular inspections are critical part of PM, as they provide
  Information for scheduling maintenance
  Information for evaluating the effectiveness of maintenance
Preventive Maintenance is component of Annual Maintenance

## Slide 14: DEFERRED MAINTENANCE
A scheduled (planned) maintenance that was not performed at the scheduled time and which was therefore put off or delayed for a future period
Made up 4 parts
  Cyclic (component replacement) maintenance
  Minor repairs not done as scheduled
  Work needed to meet laws, regulations, etc as long as the original intent of the asset has not been changed
  Functional obsolescence, e.g. A garage, or a workshop that is no more needed as such, and has to be converted to an office

## Slide 15: OPERATIONS & MAINTENANCE (O & M)
Activities and resources, required to operate and maintain facilities at a level of quality which meets the objectives of the farm, organisation etc.
The respective functions of O & M are interrelated
  it is no longer possible or desirable to consider the functions of O as separate from the functions of M
  Efforts to reduce the cost of one function may lead to an increase in the cost of the other, and all savings could be lost
Costs associated with O & M are generally recurrent, as opposed to capital investments, which are generally one-time and non-recurrent

## Slide 16: O & M (contd.)
4 alternatives of O & M:
  Operate the equipment until it breaks down – then scrap it and buy a new one (replacement instead of maintenance)
  Operate the equipment and then sell it before it either breaks down, or requires expensive overhaul (planned replacement)
  Operate the equipment until it breaks down – then repair it (breakdown maintenance)
  Carry out regular maintenance, planned carefully in conjunction with operational requirements to prevent the failure of the equipment during operations (preventive maintenance)

## Slide 17: FORMS OF MAINTENANCE
Replacement instead of maintenance: Possibilities
  Cost of repairs exceeds cost of replacement
  Technological advancement causes equipment to become obsolete rapidly
    Therefore, equipment not designed to last
  Some items are impossible to repair or designed not to be repaired
    Their value lies in their cheapness

## Slide 18: FORMS OF MAINTENANCE (contd.)
Planned replacement
  Applied in industries where equipment operate as separate units
    Machine tools, mobile generators, mobile compressors, motor vehicles, etc
  Good quality equipment is purchased and only given the basic maintenance (lubrication, servicing and adjustment), then sold, traded in or scrapped before it looses operational efficiency (when breakdowns or failures are expected)
  Can reduce downtime caused by breakdowns, prevent costly overhauls & minimise maintenance
  Important in industries where technology changes rapidly
  Can also be applied in part,
    e.g. Engine replacement, gearbox replacement

## Slide 19: FORMS OF MAINTENANCE (contd.)
Breakdown maintenance
  Used where
    equipment operate as individual unit or are separate from the main operations so that failure would not immediately or greatly affect the overall process or cause any safety hazard
    the cost of preventing failure may be more than the cost of breakdown, e.g. Sewing machines, Bench tools
  The broken down equipment (or that whose efficiency has now become too low so that it is no more productive) is replaced with stand-by reconditioned ones
  The old machine is then, in turn, repaired or reconditioned and kept in stock as future replacement part

## Slide 20: FORMS OF MAINTENANCE (contd.)
Preventive Maintenance
  Advantageous where
    the operation continues on a tightly planned schedule
    the cost of breakdown can be extremely high
    breakdowns can be extremely hazardous
  Aim is to effect the work of inspection, servicing and adjustment in order to prevent failures
  Failures must be anticipated and the necessary preventive action adopted before they occur
  Can be carried out during operation or shut-down period

## Slide 21: PLANNING AND ORGANISING MAINTENANCE & REPAIR
Planned maintenance
  Application of maintenance tackled in a scientific manner
  Work organised and carried out with forethought
  May include any or all the forms of maintenance (replacement methods, breakdown and preventive)

## Slide 22: PLANNING AND ORGANISING THE MAINTENANCE & RAPAIR (contd.)
The maintenance policy must be carefully considered
The application of the policy must be planned in advance
The work must be controlled and directed to conform to the pre-arranged plan
Historical and statistical records must be compiled and maintained to help assess the results and to provide a guide for future policy

## Slide 23: PLANNING AND ORGANISING THE MAINTENANCE & RAPAIR (contd.)
When a policy of planned replacement is used, the planning is dominated by financial considerations
    Money must always be available for the purchase of new equipment
    The sale or trade-in of old equipment must be negotiated at most affordable price, etc
However, the greater part of planned maintenance is the engineering aspect of maintenance and its relationship to the other activities of the farm (or organisation)

## Slide 24: PLANNING AND ORGANISING THE MAINTENANCE & RAPAIR (contd.)
As fundamental basis, one should decide in advance
  The individual items of the equipment to be maintained
  The form, method and details of how each item is to be maintained
  The tools, replacements, spares, tradesmen and time needed to carry out the maintenance
  The frequency at which the maintenance operations must be carried out
  The method of administering the system
  The method of analysing the results

## Slide 25: PLANNING AND ORGANISING THE MAINTENANCE & RAPAIR (contd.)
Thus, to form the structure of a practical system, there must be
  A schedule of all the equipment to be maintained
  A complete schedule of all the individual tasks that must be carried out on each item
  A programme of events that the work listed in the programme is carried out
  A method of ensuring that the work listed in the programme is carried out
  A method of recording the results and assessing the effectiveness of the programme

## Slide 26: PLANNING AND ORGANISING THE MAINTENANCE & RAPAIR (contd.)
A well organised, permanent system of documentation is essential
The document must be capable of indicating
  What is to be maintained
  How it is to be maintained
  When it is to be maintained
  Effectiveness of the maintenance

## Slide 27: BENEFITS OF PLANNED MAINTENANCE
Benefits of planned maintenance depend on
  The type of industry
  The local conditions
  The depth & scope of maintenance
  Form of application
Planned maintenance is not a panacea for every maintenance problem
  it will not compensate for
    Poor workmanship
    Lack of tools
    Bad design
    Maloperation of machinery by personnel
  It will not convert worn-out obsolete equipment into modern, highly efficient units

## Slide 28: BENEFITS OF PLANNED MAINTENANCE (contd.)
However, planned maintenance offers
  Greater availability of equipment
    Fewer breakdowns
    Maintenance carried out at most convenient time
    Less downtime than infrequent ad hoc maintenance
    Reduced length of downtime, as spare and equipment are known in advance and are available when needed
  Cheaper servicing (as those servicing are regular & simpler) than sudden expensive stop gap repairs
  Continuously high level of operational output, quality, performance and efficiency

## Slide 29: BENEFITS OF PLANNED MAINTENANCE (contd.)
  4. Greater and more effective labour utilization
    The volume of maintenance work is planned so that it is spread evenly throughout the year, and widely fluctuating demands on labour force is reduced.
    The weekly workload is known in advance so that its allocation can be controlled effectively.
    The effectiveness of a positive maintenance policy is frequently reflected in an improved personal attitude of the staff. A purposeful approach – a high morale.
  5. Alertness of servicing and adjustments times (i.e. Servicing and adjustments contained in the programme are not overlooked or omitted.)

## Slide 30: BENEFITS OF PLANNED MAINTENANCE (contd.)
Other (indirect) benefits from the documentation
  Improved budgetary control – realistic budgets can be formulated and subsequently controlled.
  Improved stock control of spares – realistic quantities of spares are stocked and re-ordered.
  Provision of information upon which management can make realistic forecasts and decisions
  Focusing attention on frequently recurring jobs and types of defect, and the type, frequency and cost of individual repairs

## Slide 31: BASIC MECHANICS OF PLANNED MAINTENANCE
Initiating the scheme
  Scheme initially originates from the Management level
  Upper Management does not formulate the exact details or operation procedures
  Upper Management must however define clearly
    the maintenance objectives
    the framework of operation

## Slide 32: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Initiating the scheme (contd.)
  Management appoints a person to whom the task is delegated
    e.g. Works Engineer, Chairman of Maintenance Committee
  The Works Engineer (or the one responsible)
    Interprets the Management policy in a manner intended
    Must be given a comprehensive brief about the policy

## Slide 33: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Initiating the scheme (contd.)
  The Works Engineer (or the one responsible)
  Must be shown
    the boundaries within which he can operate
    The results he is expected to achieve
    A programme of target dates
    The resources at his disposal
  Must be given, within the limits of his brief,
    Authority to make decisions
    Power to carry out the decisions
  Must be made responsible for actions taken

## Slide 34: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Initiating the scheme (contd.)
  The Engineer’s appointment, together with the proposed maintenance procedures may initially create speculations, resentment, resistance etc. with staff
  Necessary steps must be taken initially to avoid that before a problem escalates
    Consult and inform staff at the very beginning
    Keep staff in the picture as the scheme progresses
    Note the timing and method of his introduction
    The Engineer must watch his own personal approach

## Slide 35: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Initiating the scheme (contd.)
  The Works Engineer must initially
    Make general appraisal of the situation
    Survey the task in hand and available resources
    Work out a tentative approach to enable him apply the planned maintenance procedures in a manner that suits the system
  Even if the Engineer is already a staff, the above tasks could
    Enable him to have a fresh look
    Conceive new ideals and solutions for old familiar problems

## Slide 36: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The Inventory
  Inventory is a list of all facilities (or parts of a site, building and contents) for the purpose of identification
  This can sometimes be obtained from readily available source, if records have already been kept
  However, the records may require some corrections, as
    Some additions, deletions, replacements or movements may not have been previously recorded
    Some layout drawings may not be entirely accurate
  Plans must be based on facts
    What is actually there, not what is supposed to be there

## Slide 37: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The Inventory (contd.)
  An inventory sheet must be prepared (with additional columns to allow for additions) and filled
  The sheet normally has
    Identification symbol
      Each item must have a positive means of identification
    Description of Facility
      A brief description of the items concerned (sometimes with name plates)
    Location
      The department, section or area, in which the item is located, e.g. machine shop, boiler house, compressor room
    Type
      e.g. Mechanical, electrical or sometimes with more detailed classification
    Priority rating
      Indicating the relative importance of each item

## Slide 38: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Identification of Equipment
After inventory, it becomes essential to identify each item positively (especially in large workshops)
  So that there can be no mistake about which particular item is being referred to
  To identify and relate the respective items with their relevant documents, and vice-versa
  To locate the whereabouts of the respective items within the site
  To indicate the department, section, group or type of item for cost allocation purposes

## Slide 39: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Identification of Equipment (contd.)
Identification is done using codes made up of
  Colours, shapes, patterns, names, letters, numbers, or a combination of any of the above
The equipment must be clearly marked, and the marks must be standardised where possible
The mark must be neat, visible and indelible
It must, however, not
  Impair or stress the item or part to which it is attached
  Cause obstruction, inconvenience or any hazard

## Slide 40: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The Facility Register
  The facility register is a record of facilities, including their technical details of equipment
  Description of items to be maintained are obtained from the facility register
  The information from the facility register on each item
    Normally confirms the original specification, performance, manufacturers recommended limits, fits, tolerance
    Helps in the ordering of correct spares & replacements
    Provides the necessary information for planning the movement, relocation, access, safe floor loading, and layout of the workshop/unit

## Slide 41: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The Facility Register (contd.)
  In compiling the register, one must decide on the following
    The nature of information that will be recorded
    How the information will be recorded
    How the recorded information will be stored
    How the register will be formed
  Registers have for sometime been made of sheets or cards
    Normally one card or sheet for each item
    Each sheet or card must bear the identification symbol of the item or equipment being referred to
    The sheets are filed together into books and the cards are kept together as flat trays

## Slide 42: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The Facility Register (contd.)
  Limitations to the use of sheets or cards
    Large spaces are required, especially in large firms
    Retrieval of information has to be done manually
    This at times, can be very time-consuming, daunting, tedious
    It is also subject to mistakes
  The activities with the facility register could be better enhanced by a fully computerised data storage and retrieval system
  This occupies less space
  But this is some how costly, and one has to be trained on the Software of the system, with additional cost implications

## Slide 43: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Maintenance schedule
  Maintenance schedule is a complete list of maintenance and its incidence
  It indicates how the equipment is to be maintained
    After the details have been gathered in the facility register
  Must set out
    All the tasks
      Inspection, lubrication, adjustments, component replacement, overhaul
    Frequencies that are considered necessary to maintain the facility efficiently
  Takes into account the function of equipment and the influence it exerts over the whole operation

## Slide 44: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Maintenance schedule (contd.)
Maintenance schedule for each equipment has
  Name and identification no. of equipment
  Location of the item
  Reference no. of the schedule
  Safety procedures to be followed
  Detailed list of tasks to be carried out
  Frequency at which each task must be carried out
  Tradesmen/personnel required to undertake the tasks
  Time required to carry out the task
  Special tools or equipment required
  Materials, major components or replacements required
  When the facility is available for maintenance
    running maintenance, shut down maintenance, etc.
  Associated equipment or facilities that should be maintained simultaneously
  Details of any contract maintenance

## Slide 45: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Maintenance schedule (contd.)
  Information should be extracted and acted upon so that
    Spares, replacements, tools, special equipment and other necessary items could be ordered on time
    Maintenance contractors could be contacted and all the necessary pre-arrangements could be made and confirmed so that all parties know what is expected of them and are in agreement

## Slide 46: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Job specification
  A document describing the work to be done
  A means of communicating the work details to the persons who will effect the work (i.e. a link between the planner and the doer)
  Each task listed in the maintenance schedule should have its own separate document(s) specifying the work to be done
  The most elementary form of job specification is a direct extract from the maintenance schedule
    E.g. withdraw and clean pistons, check that rings are free and the wear is within the recommended tolerance
  Information could also be obtained from the manufacturer’s manual
  Otherwise, one has to rely on previous experience, personal judgement, etc.

## Slide 47: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Job specification (contd.)
  Job specification is done basically to ensure that:
  The task or job is carried out in the manner intended
  The possibility of omitting an operation is minimized
  Acceptable limits of wear, etc. and tolerances are clearly defined
  The tradesman or operator knows the work and how it is to be done
  The operation is always carried out in the same manner and the same allowances are always applied (standardization)
    Checking for wear, etc., is carried out in the same position and in the same way
    Results over the course of time are all comparable
  All persons doing the work, even for the first time, follow the same procedure (continuity)
  A reference standard is available with which the job and work content can be compared to detect any variation

## Slide 48: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Job specification (contd.)
  What to include in a job specification:
  The identification no. and name of the item of equipment
  The location of the item
  The maintenance schedule reference no. (and task reference) from which the task is extracted
  The job specification reference no.
    Each job specification must have its own reference no.
  The frequency at which that particular task must be carried out
  The trade or trades required to carry out each operation
  The specific details of the work to be done
    The particular method, details of inspections, tests, servicing, etc., allowable limits and tolerances
  Components to be replaced

## Slide 49: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Job specification (contd.)
  What to include in a job specification (contd.):
  Special tools and equipment to be used
  Reference drawings, manuals, etc., applicable
  Safety procedures to be followed
There should also be a footnote to the effect that:
  Any minor defect observed in the course of the specified work but not listed for attention should, if possible, be corrected and reported. If it is not possible or convenient to correct the defect in the course of the specified work it should still be reported. If the defect is considered sufficiently serious it should be brought immediately to the attention of the authorities.

## Slide 50: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The maintenance programme
  A list allocating specific maintenance to a specific period
    Having established what is to be maintain, how it is to be maintained, it must now be determined when (or within what period) it is to be maintained
  The main purpose of the maintenance programme:
  To set out a plan of work
    To spread the maintenance work load evenly over the year
    To ensure that no facility or maintenance task is omitted
    To ensure that the required maintenance is carried out at the specified frequency
    To co-ordinate the maintenance of associated facilities
    To co-ordinate the maintenance with operational requirements
  To present an overall picture of maintenance work, present and future commitments (on short and long term basis)
    To assist forward planning, ordering of spares, future labour requirements, basis for budgetary control

## Slide 51: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
The maintenance programme (contd.)
  The main purpose of the maintenance programme (contd.):
  To act as a reminder of future maintenance events (on a short term basis)
    To formulate weekly work plans (for immediate future)
    To arrange for availability of equipment for operation
    To arrange or check availability of labour, spares, sub-contractors, etc.
      The maintenance programme has flexible time span, usually on an annual basis
      The programme is normally prepared in consultation with the operators who are able to advise on schedules of operations
      The programme must ensure that the planned downtime for the shut down maintenance is considerably less than the downtime previously experienced
      A time allowance must be included for unexpected contingencies
      The plan must also allow for quick modification

## Slide 52: BASIC MECHANICS OF PLANNED MAINTENANCE (contd.)
Planning Charts
    Chats with time scale, usually in days or weeks, marked along the top edge
    Depict the work in progress and future commitments
    Present various maintenance programmes with colour coded pins, pegs or crayons
    The required maintenance and maintenance intervals are entered in appropriate columns (with allowance for holiday periods)
    Ensure that
      Every operation falls within the specified time limit
      The periodic (e.g. weekly) maintenance load is as nearly constant as possible

## Slide 53: LEVELS OF MAINTENANCE
Unit Maintenance:
  Maintenance which an organisation has responsibility to perform on its own equipment
  Subdivided into
    First level (operator)
    Second level (trained maintenance personnel)
Direct support
  Performed by Trained Mechanics and Artisans or Units (Departments) responsible for general maintenance
“return to user basis”

## Slide 54: LEVELS OF MAINTENANCE (contd.)
Technical assistance to unit maintenance elements
Reparable exchange of serviceable items for unserviceable
General support
  Maintenance support provided on an area basis
  Overhaul at this level
Equipment repaired returned to supply system
“return to user” beyond scope of local garage
Repair part stocked for General Service maintenance