## Slide 1: AE 482
Unit 1: Engineering Materials
Farm Machine Design
Mr. Joseph AVEYIRE
aveyire@yahoo.com // 024 4652593

## Slide 2: UNIT 1: Introduction
This unit describes engineering materials and determines factors that affect the choice of engineering materials:
Section 1-2 handles engineering materials
Section 2-2 tackles factors considered in choosing engineering materials

## Slide 3: UNIT 1: Learning Objectives
Classify engineering materials
Identify properties of engineering materials
Determine engineering requirements of materials
Explain the effect of strength of materials
Explain the effect of material cost
Explain the effect of engineering manufacturing processes
Effect of life span and light weight of component

## Slide 4: UNIT 1: Engineering Materials
Definition: A material is that out of which anything is or may be made of. A material relates itself to matter.
Based on chemical make-up and atomic structure, solid materials are grouped into:
Metals
Ceramics, and
Organic materials

## Slide 5: UNIT 1: Engineering Materials
some materials fall between certain categories and
some have been engineered
Examples are:
Composites, semiconductors and biomaterials
Smart (or intelligent) materials: utilized in high-technology (or high-tech)
Nano-engineering materials (very recently developed)

## Slide 6: UNIT 1: Engineering Materials
Materials used in the design and manufacture of products include:
Plastics
Wood
Composites
Ceramics
Metals
Fabrics
Acrylic lens
Balsa wood model
Layers of polycarbonate, aluminium & acrylic
Tungsten carbide tool bit
Steel, aluminium
Linen, cotton, nylon, Kevlar

## Slide 7: UNIT 1: Engineering Materials
Engineering materials can be broken down based on specific criteria as shown in Figure 1.1:
Figure 1.1: Designation of engineering materials

## Slide 8: UNIT 1: Metals
Metals easily provide an electron during bonding and electrical conductivity.
Metals are crystalline in nature
There are two groups of metals:
Ferrous : Cast iron, Steel etc.,
Non-ferrous: Cu, Al, Zn, Sn etc.
Desired properties of metals are often found in alloys

## Slide 9: UNIT 1: Metals
Metals generally possess certain characteristics :
Good thermal and electrical conductivity,
Lustre, Malleable
High strength and Formable
Metals can be:
Crystalline
Amorphous
Quasi-crystalline

## Slide 10: UNIT 1: Ceramic Materials
Ceramics are crystalline compounds of metallic and non-metallic elements, examples include:
Oxides (alumina – insulation and abrasives, zirconia – dies for metal extrusion and abrasives)
Carbides (tungsten-carbide tools)
Nitrides (cubic boron nitride, 2nd in hardness to diamond)

## Slide 11: UNIT 1: Ceramic Materials
Graphite is also categorized in ceramics
Characteristics of ceramics:
Brittle,
Hardness,
Abrasiveness
High temperature strength
Examples: Sand, Concrete, Glass, Boron nitrate etc.

## Slide 12: UNIT 1: Organic Materials
They are polymeric materials composed of long molecular chains of carbon compounds. Polymers are solids
Characteristics of organic materials:
Light weight,
Ductile,
Combustible
Examples: Rubber, Plastics, Wood, Lubricants, Textiles etc.

## Slide 13: UNIT 1: Organic Materials (Polymers)
Polymers can be classified as:
Thermoplastic
Thermoset
Elastomers
Thermoplastics | Thermosets | Elastomers
Acrylics | Epoxy resins | Rubbers
Nylons | Phenolic | Silicones
PVC | Polyesters | Polyurethanes
Polyethylene |  | 
Polyethylene
PVC gutters
Phenol formaldehyde
Urea formaldehyde
Rubber
Rubber

## Slide 14: UNIT 1: Organic Materials
Wood can be further categorised as:
Hardwood
Softwood
Manufactured board
Hardwood | Softwood | Manufactured Board
Oak | Pine | Plywood
Ash | Cedar | Blockboard
Beech | Fir | MDF
Sycamore | Spruce | Melamine board
Mahogany
Oak
Ash
Beech
Cedar
Chipboard with Veneer
Plywood

## Slide 15: UNIT 1: Properties of Materials
It is a factor that influences the qualitative or quantitative response of a given material to imposed stimuli and constraints such as forces, temperatures, etc.
It is independent of the dimension or shape.
In principle, they have a statistical behavior,
Categories of properties include:
Mechanical
Thermal
Electrical, etc.

## Slide 16: UNIT 1: Mechanical Properties
They are characteristics of a material that describe its behaviour under the action of external forces.
Knowledge of mechanical properties of materials is essential in construction of mechanically sound structure.
Examples:
Strength: to sustain loads (tension, shear, bend),
Stiffness: to resist elastic deflection (E)
Ductility: ability to undergo tensile deformation,
Hardness: resist plastic deformation-indentation.

## Slide 17: UNIT 1: Chemical Properties
They characteristics the response of a material to chemicals
Examples:
Corrosion resistance
Chemical composition,
Acidity or alkalinity
Solubility, etc.

## Slide 18: UNIT 1: Physical Properties
They are employed to describe a material under conditions in which external forces are not concerned.
Examples:
  Dimensions (i.e., size and shape) of the material.
  Density
  Porosity
Structure, etc

## Slide 19: UNIT 1: Engineering Requirements of Materials
Fabrication requirement is the ease to shape the material (machinability, ductility, castability, Weldability, heat-treatability).
Service requirement is the ability of the material to stand up to service condition of strength, wear, corrosion etc.
Economic requirement demand that the engineering part should be made with minimum overall cost

## Slide 20: UNIT 1: Factors that Affect Choice of Materials
Strength of material,
Cost of material,
Type of manufacturing process,
Form or profile of part,
Life span and light-weight

## Slide 21: UNIT 1: Strength of Engineering Materials
A material is expected to guarantee against strength failure:
Type of stress (tensile, bending, torsion etc.)
State of stress (static, dynamic, complex)
Environment (corrosion, erosion, cavitation)

## Slide 22: UNIT 1: Cost of Materials
Direct cost a material depends on:
Quality (chemical composition ) of material required,
Quantity (mass or volume) of material required,
Efficient utilization of raw material during manufacturing (minimum loss).
Quality of material is directly factored into pricing of material:
Specific material cost,
Specific material cost of reference material,
Relative material cost,

## Slide 23: UNIT 1: Strength and Cost
Example: For the cold rolled round steels, St37-2 and St50-2, deduce an expression which shows the cost-bending strength relationship. Which of the two materials will be suitable?
 | k*v | Rp0,2 (N/mm2) | b[N/mm2]
St 32- 2 | 1.0 | 240 | 340
St 50-2 | 1.1 | 300 | 420

## Slide 24: UNIT 1: Strength and Cost
Solution:
Cost of the part=weight x specific material cost
Bending strength, :

## Slide 25: UNIT 1: Strength and Cost
 |  |  |  |  | Bending
St 32- 2 | 1.0 | 240 | 340 | 0,42 | 2,1
St 50-2 | 1.1 | 300 | 420 | 0,37 | 2,0
St 32- 2 | 1.0 | 240 | 340 | 0,42 | 2,1
St 50-2 | 1.1 | 300 | 420 | 0,37 | 2,0
St50-2 is suitable

## Slide 26: UNIT 1: Engineering Manufacturing Processes
Technological properties of a material must correspond to the manufacturing process selected.
Example, weldability requires a carbon content less than or equal to 0.22% .
Table 1-2: Manufacturing requirements of manufacturing processes
.
.
.
Process | Property | Required of the material
Casting | Castability | low liquefying & solidifying temp. good form filling ability (form thin fluid layer, less shrinkage and less surface tension of the melted fluid). less tendency towards blowhole and gas bubble formation (less gas dissolving ability and less shrinkage of the liquid). less internal tension due to shrinkage when solidifying.
Rolling Forging Pressing | Malleable | good form yielding capacity (lower cold or warm yielding strength). good sliding ability of the grain structure (cubic face centred or body-centred cubic metallic lattice)

## Slide 27: UNIT 1: Engineering Manufacturing Processes
Number of elements to be produced also determines the indirect manufacturing process due to cost reason (Fig 1-4).
Figure 1-4: Cost of manufacturing processes and number items produced

## Slide 28: UNIT 1: Form (Profile / Section) of a Part
Factors that determine the form of a part:
Function of the element,
Stress distribution and
Strength of material (Favourable and unfavourable stress capability)
Optimal form of a part utilizes the favourable stress ability of the material to compensate the unfavourable stress distribution.

## Slide 29: UNIT 1: Form (Profile / Section) of a Part
Example:

## Slide 30: UNIT 1: Life Span and Light-Weight Design
Machine parts are generally subjected to dynamic loading and therefore are designed based on fatigue strength of the material
A part therefore subjected to varied stresses will experience different life cycles (Fig 1-5)

## Slide 31: UNIT 1: Life Span and Light-Weight Design
Household implements, military automobiles, weapons, computers, mobile phones etc. are designed based on short-time strength of the material due to fast technological development
Some measures against material losses:
Rust resistant material against aggressive medium.
Provision of outer coating against bad weather.
Running-in bearings against frictional wear.
Prevent pitting on gears.

## Slide 32: UNIT 1: Life Span and Light-Weight Design
For the same functional ability, light-weighted parts are preferred for the following reasons:
High driving power by automobiles {P = f(n) i.e. high speed}
Low power requirements by machines with low reduced initial masses.
Low operational cost by automobiles (minimum fuel).
Light construction can be achieved by:
Creating favourable boundary conditions
Choice of an appropriate profile and form
Choice of an appropriate material

## Slide 33: Thank You
For any concerns, please contact
elearning@knust.edu.gh
elearningknust@gmail.com
0322 191132