## Slide 1: AE 482
UNIT 3: Engine Performance Characteristics
Agric Engineering Design Project
Mr. Joseph AVEYIRE
aveyire@yahoo.com // 024 4652593

## Slide 2: Introduction
Unit three handles engine performance characteristics and takes a look into the tractor engine power. It
Identifies the performance characteristics of internal combustion engine, and
Considers the power that can be obtained from a tractor engine.

## Slide 3: UNIT 3: Learning Objectives
Determine the power and efficiency of an engine
Explain engine torque and efficient loading
Determine the fuel consumption of an engine
Identify sources of power from a tractor engine
Identify the various types of dynamometers
Determine procedure of testing an engine

## Slide 4: UNIT 3: Engine Performance Characteristics
Engine performance is an indication of the degree of success with which the engine performs its assigned task.
Engine performance is evaluated on the basis of:
Performance parameters and
the particular application of the engine
For example, for an aircraft engine specific weight is more important than the specific fuel consumption

## Slide 5: UNIT 3: Engine Performance Characteristics
Basic performance parameters include the following:
Power and Mechanical Efficiency.
Mean Effective Pressure and Torque.
Specific Output.
Volumetric Efficiency.
Fuel-air Ratio.
Specific Fuel Consumption.
Thermal Efficiency and Heat Balance.
Specific Weight

## Slide 6: UNIT 3: Power and Mechanical Efficiency
Indicated power is given by:
Where

## Slide 7: UNIT 3: Power and Mechanical Efficiency

## Slide 8: UNIT 3: Power and Mechanical Efficiency
Brake Torque
Of importance is the overall efficiency of an engine in converting fuel equivalent power to brake power :

## Slide 9: UNIT 3: Power and Mechanical Efficiency
Brake Torque
Thus, brake torque and mean effective brake pressure are related by the engine size
A large engine produces more torque for the same
Torque is not the measure of the ability of an engine to utilize its displacement for producing power from fuel
gives an indication of engine displacement utilization for this conversion

## Slide 10: UNIT 3: Engine Torque and Efficient Loading
Brake Torque

## Slide 11: UNIT 3: Engine Torque and Efficient Loading
Brake Torque
Note, is constant
varies little with changes in torque and speed
Therefore, indicated torque varies nearly proportionally with quantity of fuel injected into each engine cycle (controlled by engine governor)

## Slide 12: UNIT 3: Engine Torque and Efficient Loading
Efficient Loading
Figure shows the curve of against where the slope is approximately .

## Slide 13: UNIT 3: Engine Torque and Efficient Loading
  Efficient Loading:
  This implies that
  All engines are most efficient at full load and are especially inefficient as the load approaches zero
  At idle engine speed, its efficiency is zero

## Slide 14: UNIT 3: Specific Fuel Consumption
Indicates the amount of fuel burnt by the engine to accomplish a given amount of work:
Indicates the efficiency with which the engine develops power from fuel

## Slide 15: UNIT 3: Specific Fuel Consumption
Units of BSFC

## Slide 16: UNIT 3: Specific Fuel Consumption
Relationship between BSFC numbers and efficiency
LHV=Low heating value
For diesel LHV=0.0119531kWh/g

## Slide 17: UNIT 3: Tractor Power Measurements
Terminology:
Brake power is the power
Pto-power
Draw bar power
Friction power
Indicated power
Maximum brake power
Observed power
Corrected power
Rated horsepower

## Slide 18: UNIT 3: Tractor Power Measurements
Example 1:
A certain compression ignition engine consumes No.. 2 diesel fuel (Hg=45,000 kJ/kg) at the rate of 26.3 kg/h while running at a rated speed of 2200 rpm and producing 595 Nm of torque. Assuming the mechanical efficiency is 0.85.
Calculate the fuel equivalent power,
Calculate the brake power,
Calculate the indicated power,
Calculate the friction power,
Calculate the indicated thermal efficiency,
Calculate the brake thermal efficiency,
Calculate the BSFC

## Slide 19: UNIT 3: Tractor Power Measurements
Solution 1:

## Slide 20: UNIT 3: Tractor Power Measurements

## Slide 21: UNIT 3: Tractor Power Measurements
Example:
Consider an engine rated as 595 Nm,(137 kW) at 2299 rpm has an idle speed of 2400 rpm and a torque reserve of 30%; Peak torque occurs at 1300 rpm. Sketch the torque and power curves (versus engine speed).

## Slide 22: UNIT 3: Tractor Power Measurements
Solution:

## Slide 23: UNIT 3: Tractor Power Measurements

## Slide 24: UNIT 3: Types of Dynamometers
Dynamometer is an instrument for determining power usually by the independent measure of force, time and the distance through which the force is moved
Brake Dynamometers
Drawbar Dynamometers
Torsion Dynamometers
Transmission Dynamometer
Absorption Dynamometers

## Slide 25: UNIT 3: Prony Brake Dynamometer
Lock a on b by means of c
Apply force F is to arm d and give arm a complete revolution. Work done per one revolution is .
Fix arm d is fixed and give b one revolution inside the block. Work done in overcoming friction

## Slide 26: UNIT 3: Prony Brake Dynamometer
Prony Brake Constant

## Slide 27: UNIT 3: Prony Brake Dynamometer
Prony Brake Constant

## Slide 28: Example
For a prony brake dynamometer, derive the power (kW) given the force (N), rotational speed (rpm) and length of arm (m).
A two cylinder, two-stroke engine has a bore of 100mm and a stroke of 120mm. The engine develops a power of 50kW at 2200rpm when tested with a pony brake dynamometer.
Compute the length of arm (mm) necessary to give a brake constant of
Compute the brake net scale reading in Newtons, if the length, l, of the arm is 1000mm.

## Slide 29: Thank You
For any concerns, please contact
elearning@knust.edu.gh
elearningknust@gmail.com
0322 191132