## Slide 1: AE 482
UNIT 5: Hydraulic Fluids
Farm Machine Design
Mr. Joseph AVEYIRE
aveyire@yahoo.com // 024 4652593

## Slide 2: Introduction
Unit four identifies hydraulic power transmission and hydraulic fluids.
Section 1-4 Describes hydraulic fluids, and
Section 2-4 On the other hand handles hydraulic components and their applications.

## Slide 3: UNIT 4: Learning Objectives
Explains the principle of hydro-mechanics,
Describes the theory of lubrication,
Explains the classification of hydraulic fluids,
Explains the selection of hydraulic fluids

## Slide 4: UNIT 4: Introduction
Fluid Power:
Fluid power is the technology that deals with the transfer and control of energy and signal by means of pressurised fluids.
The pressurised fluid can be either liquid or gas (i.e. hydraulics and pneumatics fluid power).

## Slide 5: UNIT 4: Principles of Hydro-Mechanics
Hydraulic Transmission of Energy
There are two forms of science of hydraulics:
Hydrodynamics: deals with high velocities and low pressure (Principle of moment of momentum), and
Hydrostatics : involves high pressure and low pressures (Principles of positive displacement)
From this point onwards: Hydraulics will denote hydrostatics.

## Slide 6: UNIT 4: Principles of Hydro-Mechanics
Hydro-Mechanic Principle of Energy:
Bernoulli equation:

## Slide 7: UNIT 4: Principles of Hydro-Mechanics
Energy transformation (between Mechanical and Fluid Energy):
Steady flow:
Specific Energy flow:
Pump / Motor

## Slide 8: UNIT 4: Principles of Hydro-Mechanics
Under Hydrostatic fluid Transmission:
+

## Slide 9: UNIT 4: Principles of Hydro-Mechanics
, output is mechanical
, output is hydraulic

## Slide 10: UNIT 4: Principles of Hydro-Mechanics
Applying thermodynamics:
,
Noting that hydraulic fluids are incompressible

## Slide 11: UNIT 4: Principles of Hydro-Mechanics
Therefore,
Constant mass flow rate= const. volumetric flow rate x const. density:

## Slide 12: UNIT 4: Comparison of Energy Transmission
Comparison of Hydraulic Force/Energy Transmission to other Forms:
Criteria | Mechanical | Hydraulic | Electrical
Force Density | very good | good | bad
Transmission Distance | bad | good | very good
Control | bad | good | good
Safety | Approximately the same |  | 
Efficiency | good | bad | bad
Flexibility in structure | bad | good | very good
Cost of elements | expensive | expensive | cheap
Size | big | small | big

## Slide 13: UNIT 4: Electrical-Mechanical Energy Conversion
Advantages of Hydraulic Controls and Drives:
Force Density: Electric motor
A conductor carrying an electric electrical current in a magnetic field experiences an electrical force governed by the Fleming’s left-hand rule (As in Electric motor).

## Slide 14: UNIT 4: Electrical-Mechanical Energy Conversion
Advantages of Hydraulic Controls and Drives:
Force Density:
Electric motor:
Hydraulic motor:

## Slide 15: UNIT 4: Fluid Energy Transmission
Advantages of Hydraulic Controls and Drives:
Distance: transfer of energy within moderate distance possible with hoses and pipes,
Control: hydraulic control parameters are volumetric flow rate and pressure. There are simple standard parts available for both hydraulic and electrical transmissions controls.
Efficiency: Low due to presence of complex resistance (ohm, capacitance and inductance) in hydraulic transmissions
Size: hydraulic motors are small due to high force density.

## Slide 16: UNIT 4: Fluid Energy Transmission
Disadvantages of Hydraulic Controls and Drives:
High Losses: Due to fluid friction in flows through pipes, hoses, changes in cross-sectional area; and losses due to leakages at high pressure and clearances.
Sensitivity: Sensitive to foreign particles.
Dependence: Depends on the properties of the fluid (maxi. Temperature, compressibility)
Slip: Slip during rotation (n)
Danger: Leakages and bursting of pipes are dangers to life and property.
Low-life: The high force density results in high frictional wear

## Slide 17: UNIT 4: Fluid Energy Transmission
Applications of Fluid Power transmission:
Fluid power is pervasive
Gas springs in office chairs
Air drills used by dentists,
Brakes in automobiles,
Practically to every large agriculture, construction and mining machine including harvesters, drills and excavators.

## Slide 18: UNIT 4: Principles of Hydro-Mechanics
Hydrostatics
The principles of hydrostatics hold only under ideal fluids, which are:
Massless: no presence of kinetic energy
Frictionless: it is not viscous, and
Incompressible: volume does not change with pressure.
Therefore, experience no losses during operation.

## Slide 19: UNIT 4: Principles of Hydro-Mechanics
Hydrostatics
Fundamentals of hydrostatics is the principle of Pascal:
“The effect of a force on fluid at rest, propagates itself in all directions within the fluid. The magnitude of the pressure in the fluid is equal the loading force acting at the effective surface. The pressure acts always at right angle on the boundary surface”.

## Slide 20: UNIT 4: Principles of Hydro-Mechanics
Hydrostatics: linear motion
p
p
For ideal fluid and no leakage:
Volume:
Pressure:
Velocity:
Law of Continuity:
Work by piston:
Power:
Figure 5.5: Pascal principle for linear motion

## Slide 21: UNIT 4: Principles of Hydro-Mechanics
Hydrostatics: rotational motion
Figure 5.6: Hydrostatic drive train
Q
Pump
Motor
Tank

## Slide 22: UNIT 4: Principles of Hydro-Mechanics
Hydrostatics: rotational motion
T
High pressure
Low pressure
Figure 5.6: Model of a positive displacement machine
Ring cylinder
Piston
Volume:
For ideal fluid and no leakage:
Pump
Motor
Discharge:
Torque:

## Slide 23: UNIT 4: Principles of Hydro-Mechanics
Efficiency of ideal hydrostatic transmission:
Hydrostatics: rotational motion
Torque transfer between Pump and Motor
As in Figure 5.6, where is the same for pump and motor
For loss-free operation, the output hydraulic power is equal the input mechanical power
Where and are mechanical power
Or

## Slide 24: UNIT 4: Principles of Hydro-Mechanics
Example: A loss-free hydrostatic drive train in an opened circuit has been assigned the following data:
Q,
Pump
Motor
Tank
,
Intake volume of motor, ,
Rotational speed of pump,
Output torque,
1 bar=100,000

## Slide 25: UNIT 4: Principles of Hydro-Mechanics
For a displaced volume of the pump within the discharge range of (varying continuously), calculate , , ,
Sketch the characteristic curve and ,
If the power of the electric motor is 15 kW, at what maximum swept-volume can the pump be set?

## Slide 26: UNIT 4: Principles of Hydro-Mechanics
.50 =73.750

## Slide 27: UNIT 4: Principles of Hydro-Mechanics

## Slide 28: UNIT 4: Theory of Lubrication
Design and construction of machines are based on certain criteria such as:
Operational safety dimensioning and shaping of machine elements for a given expected life-span depend upon:
forces
Geometric form
Material of element
Guaranteed functioning of a machine depends on:
co-existence of pairing elements at the point of contact (Technical mating system=Fits and Tolerance)

## Slide 29: UNIT 4: Theory of Lubrication
Technical Mating System
The elements found within the technical mating system are:
  Primary body,
  Secondary body,
  Intermediary medium and
  Environment.
Properties of the elements are:
  Material properties of the elements,
  Form properties of the elements and
  Surface properties of the elements.

## Slide 30: UNIT 4: Theory of Lubrication
Technical Mating System
Interactions
Example primary body and environment:
Sublimation
Adsorption
Chemical reaction

## Slide 31: UNIT 4: Theory of Lubrication
Technical Mating System
Metallic Surface:
Consists of:
Impurities
Absorbed gases
Oxide layer
Cold-worked layer
Base material
On top of metallic surfaces:

## Slide 32: UNIT 4: Theory of Lubrication
Wear
It is the progressive loss of material on surface of a solid body.
It is due to contact and relative motion of a solid body to a solid, liquid or gas medium
It is recognized by:
Presence of loose particles,
Change in material properties, and
Change in form.

## Slide 33: UNIT 4: Theory of Lubrication
Factors Affecting Wear
Type of motion (sliding, rolling, impact etc.)
Trend of motion (continuous, intermittent, reversible, oscillation)
Forces/stresses (compression, tensile, etc)
Speed
Temperature
Duration or distance travelled
Properties of material
Form and nature of contact surfaces eg concave-convex surfaces, roughness

## Slide 34: UNIT 4: Theory of Lubrication
Types of Wear (Mechanisms of Wear)
Tribo-oxidation (Oxidative Wear) is the removal of oxide-layer (layer activated by surface friction, medium and environment)
Adhesive Wear is characterised by building and breaking down of “welded” bridges (First, requires the break-down of the oxide-layer)
Abrasive Wear caused either by hard tips surface-profile or by the presence of hard foreign particles
Surface Disruption (surface fatigue) characterised by micro-cracks and breaking away of surface particles due to alternating mechanical stress . E.g.. pitting

## Slide 35: UNIT 4: Theory of Lubrication
Units of Wear
coefficient of wear, k, is the most frequent applied wear characteristic parameter involving paired materials:
Where

## Slide 36: UNIT 4: Theory of Lubrication
Units of Wear
Linear wear-distance,
It is used to characterise machine wear, because depth of wear is used as a yard-stick for replacement of an element:

## Slide 37: UNIT 4: Theory of Lubrication
Stages of Wear
Regressive wear (wear-in),
Linear wear,
Progressive.

## Slide 38: UNIT 4: Classification of Hydraulic Fluids
Several criteria used to classify hydraulic fluids due to:
diverse areas of application of hydraulic systems,
diverse types of equipment available, and
increasing number /types of hydraulic fluids available.
Hydraulic fluids can therefore be classified based on:
physical properties,
chemical types,
operating capabilities,
utility, or specific applications.

## Slide 39: UNIT 4: Classification of Hydraulic Fluids
Common classification criteria of hydraulic fluids are:
Classification by chemical properties: petroleum and non-petroleum hydraulic fluids.
Classification by physical properties: viscosity
1S0-VG,
Redwood-seconds
SAE for automobiles.
Classification by operating characteristics: temperature limits and the fire-resistant characteristics (DIN 51502 and ISO 67434)

## Slide 40: UNIT 4: Classification of Hydraulic Fluids
Petroleum Based Hydraulic Fluids
They were among the first liquids employed as hydraulic fluids,
They have bases of paraffin, olefin, naphten or asphalt,
Their properties depend upon:
chemical composition (origin), and
type of raffination.
They give outstanding performance, long life, good lubricating characteristics, and protection against rust, oxidation, corrosion, sludge, and foam formation.

## Slide 41: UNIT 4: Classification of Hydraulic Fluids
ISO Classification of Petroleum based hydraulic fluids (ISO 6743-4) categorises hydraulic fluids that:
do not have any additives as HH,
contain oxidation and rust inhibitors to protect equipment from chemical deterioration and water contamination as HL,
are version of HL-type fluids with improved anti-wear additives and improved high-pressure performance as HM.

## Slide 42: UNIT 4: Classification of Hydraulic Fluids
ISO-VG (ISO Viscosity Grades)
ISO viscosity grades classify hydraulic fluids based upon their kinematic viscosity at 40OC.

## Slide 43: UNIT 4 : Classification of Hydraulic Fluids
Viscosity-temperature diagram,
Recommended Temp. Range

## Slide 44: UNIT 4 : Classification of Hydraulic Fluids
Viscosity: (ISO-VG)
Specification of ISO-VG46 implies it is an oil of the viscosity class 46
Question:
Oil with specification ISO-VG100 has a density of 900kg/m3. What is the dynamic viscosity (η)?
Answer:
at

## Slide 45: UNIT 4 : Classification of Hydraulic Fluids
SAE Viscosity Grade
  SAE VG gives no indication of quality and suitability of oil for a given application.
  According to SAE, there are two basic types of oil:
  Single grade
  Multi-grade

## Slide 46: UNIT 4 : Classification of Hydraulic Fluids
SAE Viscosity Grade
Multi-Grade:
Multi-grade oils have a flat viscosity-temperature curve,
Multi-grade oil designations consist of dynamic viscosity, at -18°C and kinematic viscosity, at 100°C

## Slide 47: UNIT 4 : Classification of Hydraulic Fluids
Example: SAE 10W-30
Has an apparent dynamic viscosity of 1500mPa.s at -18°C (SAE 10W),
Has a kinematic viscosity of 10 at 100°C (SAE30).
It overlaps three viscosity grades.
SAE Viscosity Grade | Apparent viscosity η at -18°C as per DIN 51377 (mPa.s) | Kinematic viscosity at 100°C as per DIN 51550 (mm2/s) | 
 |  | Min | Max.
5W | ...............1250 | 3.8 | 
10W | 1250..........2500 | 4.1 | 
15W,' | 2500..........5000 | 5.6 | 
20W | 5000 ........10000 | 5.6 | 
20 |  | 5.6 | 
30 |  | 9 | 12.5
40 |  | 12.6 | 16.3
50 |  | 16.3 | 21.9
SAE Viscosity Grade | Apparent viscosity η at -18°C as per DIN 51377 (mPa.s) | Kinematic viscosity at 100°C as per DIN 51550 (mm2/s) | 
 |  | Min | Max.
5W | ...............1250 | 3.8 | 
10W | 1250..........2500 | 4.1 | 
15W,' | 2500..........5000 | 5.6 | 
20W | 5000 ........10000 | 5.6 | 
20 |  | 5.6 | 
30 |  | 9 | 
40 |  | 12.6 | 
50 |  | 16.3 | 

## Slide 48: UNIT 4: Additives
Improve the properties of mineral oils based hydraulic fluids,
Types of additives:
viscosity index improver (VI),
oxidation and corrosion inhibitors,
high-pressure additives (EP), and
detergents and dispersants

## Slide 49: UNIT 4: Additives
Properties of Fluid improved by additives:
  viscosity-temperature relationship,
  resistance of the oil to aging
  corrosive protection capacity,
  load carrying capacity in the mixed frictional state,
  stock point,
  foaming tendency, and
  air releasing capacity.

## Slide 50: UNIT 4: Selection of Hydraulic Fluids
Based on compliance with the minimum requirements of DIN 51524

## Slide 51: UNIT 4: Selection Criteria of Hydraulic Fluids
Suitability of Hydraulic fluid depend on the following factors:
Density, Compressibility
Losses in pipes and canals are directly proportional to the density of the operating medium:
Volume of a fluid increases when the temperature increases. Thus, density reduces.

## Slide 52: UNIT 4 : Selection Criteria of Hydraulic Fluids
Viscosity:
It is a measure of the internal friction of the fluid.
Dynamic viscosity, η, is more of importance than the kinematic viscosity, ν, when describing the load carrying capacity of a fluid
However, fluids are classified based on their kinematic viscosity.

## Slide 53: UNIT 4 : Selection Criteria of Hydraulic Fluids
Viscosity:
Permissible viscosity range of a complete systems takes account of the permissible viscosity of all components,
Optimum operating viscosity range of each component should be kept within the permissible temperature range by:
either cooling or
heating, or both

## Slide 54: UNIT 4 : Selection Criteria of Hydraulic Fluids
Viscosity:
Viscosity at operating temperature determines:
the response characteristics of closed control loops,
stability and damping of system,
the efficiency factor and
the degree of wear,

## Slide 55: UNIT 4 : Selection Criteria of Hydraulic Fluids
Viscosity: (Viscosity-Temperature Relationship)
Viscosity drops when the temperature increases and rises when the temperature decreases,
Fluids with a low slope are suitable when used as hydraulic fluid,
A high VI means less temperature dependence

## Slide 56: UNIT 4 : Selection Criteria of Hydraulic Fluids
Determining the correct viscosity grade for a particular application: Note
Start (maximum) viscosity at minimum ambient temperature,
Minimum viscosity at maximum expected operating temperature,
Permissible and optimum viscosity range for system components.

## Slide 57: UNIT 4 : Selection Criteria of Hydraulic Fluids
Viscosity: (Viscosity-Pressure Relationship)
This relationship is responsible for the loading ability of lubricating fluids,
increase in viscosity with an increase in pressure has a self-strengthening effect.

## Slide 58: UNIT 4 : Selection Criteria of Hydraulic Fluids
Wear protection capability
Figure 4: Stribeck’s curve
Hydrodynamic lubrication requires high relative speeds between objects,
From start to final speed, the objects experience:
Solid friction state,
Mixed friction state,
Fluid friction state.

## Slide 59: UNIT 4 : Selection Criteria of Hydraulic Fluids
Wear protection capability
Hydrodynamic lubrication: is the determining factor for the protection of wear,
In mixed frictional state:
should be above a critical value, in order to
Be able to keep the two rubbing surfaces apart, and
Thus, prevent wear.

## Slide 60: UNIT 4 : Selection Criteria of Hydraulic Fluids
In mixed frictional state, should drop below a critical value and therefore unable to keep the two rubbing surfaces apart, then protection of wear would depend upon:
Chemical reactions on the surfaces,
Ability of the hydraulic fluid to spread over the surfaces, and
Presence of wear-protective additive

## Slide 61: UNIT 4 : Selection Criteria of Hydraulic Fluids
Dissolution of Gases
Pressure fluids do dissolve a certain proportion of gases,
Capacity to dissolve these gases is proportional to the pressure if the pressure is less than 300bar and
Amount of gas dissolved is expressed by Dalton equation:

## Slide 62: UNIT 4 : Selection Criteria of Hydraulic Fluids
Cavitation
Due to dissolved gases or air coming out of a fluid forming bubbles,
Even if dissolved gases are not present, the fluid may ''boil'' when its pressure becomes too low, or its temperature too high.
Evaporation or boiling occurs at atmospheric temperature when the pressure is reduced below the saturation vapour pressure,
This can result out of a higher fluid velocity,
Actual problem is the high explosive nature of these gases near surfaces when the fluid re-enters a high pressure zones.

## Slide 63: UNIT 4 : Selection Criteria of Hydraulic Fluids
Cavitation can take place in:
a. suction pipe lines and canals of pumps,
Causes: Lower absolute pressure due to:
  losses in fittings, curves, reduced cross-sectional areas,
  long suction heights,
  higher velocities.
Effects: erosion of parts, power losses, high noise, pressure shocks etc.
b. Throttles, orifices, etc.
Causes: Lower pressures due to high velocities
Effects: high noise, erosion, instability of their controls, change in the flow characteristics

## Slide 64: UNIT 4 : Selection Criteria of Hydraulic Fluids
Cavitation Protective Measures:
Choice of material with resistance to erosion on surface,
Reducing the pressure differences on a single pressure reducing element (serial connection of such elements),
Deviating the cavitation’s jet away from critical areas

## Slide 65: UNIT 4 : Selection Criteria of Hydraulic Fluids
Material compatibility
Hydraulic fluid must not negatively affect the materials of components such as coatings, seals, hoses, metals and plastics

## Slide 66: UNIT 4 : Selection Criteria of Hydraulic Fluids
Aging (oxidation and Polymerisation)
Oxidation is a reaction with oxygen to form acidic bases.
Polymerisation is the increase in the length of the C-H chain, and it leads to the formation of sludge,
Acceleration of aging can be due to:
High operating temperatures.
Presence of foreign air,
Presence of water and other impurities,
Presence of metallic catalyst (mostly Cu and Cu-alloys)

## Slide 67: UNIT 4 : Selection Criteria of Hydraulic Fluids
Aging (oxidation and Polymerisation) Neutralisation Number:
It is a scale for determining the aging state of fluids,
it specifies the amount of-KOH necessary to neutralise 1g of the fluid.

## Slide 68: UNIT 4 : Selection Criteria of Hydraulic Fluids
Air separation ability (ASA)
Property of a hydraulic fluid to separate undissolved air
Hydraulic fluids always contain dissolved air,
During operation, dissolved air may be transformed into undissolved air, leading to cavitation,
air separation capacity depends on the viscosity, temperature, basic fluid and aging,
It cannot be improved by additives.

## Slide 69: UNIT 4 : Selection Criteria of Hydraulic Fluids
Demulsifying ability and water solubility
The capacity of a hydraulic fluid to separate water at a defined temperature is known as demulsifying ability,
For larger systems with permanent monitoring, a demulsifying fluid with good water separation capability (WSC) is recommended

## Slide 70: UNIT 4 : Selection Criteria of Hydraulic Fluids
Filterability
Filterability describes the ability of a hydraulic fluid to pass through a filter, removing solid contaminants,
Filterability is a basic prerequisite for cleanliness, servicing and filtration of hydraulic fluids

## Slide 71: UNIT 4 : Selection Criteria of Hydraulic Fluids
Additivation
Properties of fluids can be modified with suitable additives,
Distinction is made for fluids between heavy metal-free and heavy metal-containing (generally zinc) additives systems,
Both additive systems are most often incompatible with each other,
Increasing additivation generally leads to deteriorated air separation ability (ASA) and water separation capability (WSC) of the hydraulic fluid

## Slide 72: UNIT 4 : Selection Criteria of Hydraulic Fluids
Measures taken when changing type of fluid:
thoroughly cleaning of the plant,
Replacing the seals,
Inspect / test the suction behaviour, filter and container construction,
Inspect the paintings of the container

## Slide 73: Thank You
For any concerns, please contact
elearning@knust.edu.gh
elearningknust@gmail.com
0322 191132