## Slide 1
MME 351 - Marine Electrical Technology
(2 0 2)
E.A. Frimpong (PhD), MIEEE, MGhIE
Associate Professor at Department of Electrical and Electronic Engineering,
Kwame Nkrumah University of Science and Technology, Kumasi, Ghana

## Slide 2: Course aim
To provide insight into electrical technology used in marine vessels.
KNUST-SESC

## Slide 3: Course Content
Power generation and distribution: Selection of DC and AC generators, Merits and Demerits of AC and DC. Construction & Characteristics of brushless high speed AC generators with automatic Voltage regulator.
Rules and Regulations governing electrical machinery on ships, location and installation of generator sets. Rating and characteristics of main switch boards. Arrangements of preferential trips and protective devices with wiring diagrams.
System earthing: Isolated neutral systems, resistance earthed system.
KNUST-SESC

## Slide 4: Course Content
Motor and Control Equipment: Special requirements of motors and starters for anchor Windlass & Capstan, wiring diagram, lowering & hoisting arrangement, overload protection, magnetic disc, brakes. Centralised control of motors in machinery spaces. Classes of insulation (A, B and E) and Temperature rise.
Starters for miscellaneous electrical equipment for machinery space auxiliaries eg. Sequential starting and cut outs for an automatic fired boiler incorporating safety devices & combustion control equipment. Sequential starting for refrigerating plants, incorporating safety devices like high pressure cut out, cooling water failure cut out, automatic defrosting with help of timer.
KNUST-SESC

## Slide 5: Assessment
Continuous assessment (Assignments, quizzes, mid-sem) - 30%
End-of-Semester Examination (MCQs, Written paper) - 70%
KNUST-SESC

## Slide 6
Power Generation
and
Distribution in Marine Vessels
KNUST-SESC

## Slide 7: Uses of electricity in watercraft
KNUST-SESC
Lighting
Refrigeration
Pumps

## Slide 8: AC generators
KNUST-SESC
Operating principle of AC generators

## Slide 9: AC generators
KNUST-SESC
Types AC generators
3-phase AC generator
1-phase AC generator

## Slide 10: AC generators
KNUST-SESC
Major components
Stator
Rotor
Slip rings

## Slide 11: AC generators
KNUST-SESC
Stator

## Slide 12: AC generators
KNUST-SESC
Rotor

## Slide 13: AC generators
KNUST-SESC
Slip rings

## Slide 14: DC generators
KNUST-SESC
A DC generator is essentially a 1-phase AC generator with commutator

## Slide 15: AC vrs DC generators
KNUST-SESC
DC Generators
Suitability for large motors
Simple design
AC Generators
Suitability for electrical appliances and small motors
Low maintenance needs
Easy distribution of the output with a transformer
Higher efficiency
Losses are relatively fewer than DC Generators
AC generators can be easily stepped up and stepped down through transformers.
Smaller in sizer compared to DC generators.

## Slide 16: Emergency power supply
KNUST-SESC
Emergency power is needed when the main supply system fails.
Emergency power can be supplied by
Batteries
Emergency generator
Both batteries and generator
Emergency power should cover the following key components and systems
Steering gear system
Emergency bilge pump
Watertight doors
Fire fighting system
Ship’s navigation lights and emergency lights
Communication and alarm system

## Slide 17: Location and installation of generators
KNUST-SESC
A solid, level mounting platform is necessary
Adequate space on all sides for ventilation and servicing
Generators must be kept away from living quarters, and away from bilge splash and vapors.

## Slide 18: Emergency power supply
KNUST-SESC
Emergency generator is normally located outside the machinery space to provided unhindered access to it.

## Slide 19: Electrical distribution systems
KNUST-SESC
The power distribution system of a ship is designed to provide a secure supply to all loads with built-in protection for equipment and personnel.

## Slide 20: Electrical distribution systems
KNUST-SESC
A ship’s electricity distribution system consists of different component for distribution and safe operation of the system. They are:
Ship generator consisting of prime mover and alternator.
Main switch board which is a metal enclosure taking power from a generator and supplying it to different machinery.
Bus Bars which act as a carrier and allow transfer for transfer of power from one point to another.
Circuit breakers which act as a switch and in unsafe condition can be tripped to avoid breakdown and accidents.
Fuses as safety device for machinery.
Transformers to step up or step down the voltage.

## Slide 21: Electrical distribution systems
KNUST-SESC
Generator

## Slide 22: Electrical distribution systems
KNUST-SESC
Main switch board
Domestic
Ship

## Slide 23: Electrical distribution systems
KNUST-SESC
Busbars

## Slide 24: Electrical distribution systems
KNUST-SESC
Fuse

## Slide 25: Electrical distribution systems
KNUST-SESC
Circuit breaker

## Slide 26: Electrical distribution systems
KNUST-SESC
Transformer

## Slide 27: Electrical distribution systems
KNUST-SESC
A typical distribution system for a ship

## Slide 28: Emergency switchboard
KNUST-SESC
It is the emergency power distribution center.
It distributes power to auxiliaries that are vital, under emergency conditions
Under normal operation, power for the emergency switchboard is supplied by the main generators through a bus-tie.
In case of power failure, loss of voltage at the emergency switchboard will cause the emergency generator to automatically start.
Simultaneously, the bus-tie will open disconnecting the main and the emergency switchboards.
The emergency generator breaker will close, energizing the emergency board and providing the needed emergency power.

## Slide 29: Electrical distribution systems
KNUST-SESC

## Slide 30
KNUST-SESC
Ship’s distribution system

## Slide 31
KNUST-SESC

## Slide 32: Electrical distribution systems
KNUST-SESC
Ship shore supply

## Slide 33: Motors
KNUST-SESC

## Slide 34: Motors
KNUST-SESC
Uses
Electric propulsion

## Slide 35: Motors
KNUST-SESC
Windlass

## Slide 36: Motors
KNUST-SESC
Winches

## Slide 37: Motors
KNUST-SESC
Pumps

## Slide 38: Motors
KNUST-SESC
Fans

## Slide 39: Motors
KNUST-SESC
Classes of motors

## Slide 40: Motors
KNUST-SESC
Motors used in marine vessels
Induction (Asynchronous ) Motors
Synchronous motors

## Slide 41: Induction Motors
KNUST-SESC
They are the workhorses of marine vessels

## Slide 42: Induction Motors
KNUST-SESC
They are either single-phase or three-phase type

## Slide 43: Induction Motors
KNUST-SESC
Single-phase induction motors
They are powered by single-phase power supply.
They are mostly used in low power applications such as small pumps, small portable compressors and small fans.

## Slide 44: Induction Motors
KNUST-SESC
Three-phase induction motors
They are supplied with 3 three-phase AC supply
They are of two types, namely, squirrel cage and wound rotor.
Squirrel cage motors are widely used on ships due to their rugged construction and simple design.
Typical applications of three-phase induction motors are: lifts, cranes, large capacity exhaust fans, engine auxiliary pumps, engine blower fan motor, engine room heavy load pumps including pumps for fire-fighting, freshwater and sea water.

## Slide 45: Induction Motors
KNUST-SESC
Advantages of induction motors
They are robust and simple in construction, with few moving parts.
They can efficiently operate in a rugged and harsh environment such as in seagoing vessels.
The maintenance cost of 3-phase induction motor is less; they do not have parts like brushes, commuters or slip rings.
An induction motor can operate in an intrinsic environment as they do not have brushes which can cause sparks that could ignite fire.
3-phase induction motors do not need additional starting mechanism or arrangement as they can generate self-starting torque

## Slide 46: Induction Motors
KNUST-SESC
Disadvantages of induction motors
During starting, they draw high starting current, particularly when attached to a heavy load. This causes a dip in voltage during the starting period of the machine.
Induction motors operate at lagging power factor which results in increased power losses and efficiency reduction, especially at low load.

## Slide 47: Induction Motors
KNUST-SESC
Potential faults
Environmental faults
Moisture in air
Vibration from heave equipment
Winding faults due to insulation failure
Unbalance supply due to blown fuses
Crawling due to harmonics in supply
Imbalance rotor due to defect in the rotor, internal misalignment, bending of the shaft, uneven loading and improper motor and load coupling.

## Slide 48: Induction Motors
KNUST-SESC
Fatigue failure due to improper maintenance, use of poor quality parts, weakening of material caused by repeated load applications.
Bearing failure due to poor maintenance, due to overloading, wrong installation, contaminated lube oil, operation at excessive temperature and water in lubrication (grease).
Lubrication problem due to lack of lubrication or contamination of lubricants leading to can lead to increase friction between parts and bearings.

## Slide 49: Induction Motors
KNUST-SESC
Protection of induction motors
Overload protection
Overcurrent protection
Phase unbalance protection
Stalling (locked rotor) protection

## Slide 50: Induction Motors
KNUST-SESC
Starting of induction motors
Direct-on-line starting
Resistance starting
Auto-transformer starting
Star-Delta starting